Hardware Design Description

Plantation Productions Open Source/Open Hardware Data Acquisition System

Table of Contents

1	Introduction	4

1.1	Purpose	4

1.2	Scope	4

1.3	Contents of the Document	4

1.4	Document Conventions	4

2	Hardware Architecture	6

2.1	Design Considerations	7

2.1.1	Assumptions and Dependencies	7

2.1.2	Related Software or Hardware	7

2.1.3	End-User Characteristics	7

2.1.4	System Interfaces	7

2.1.5	Fail-Safe	8

2.1.6	Hardware Basis	8

2.1.7	User Interfaces	8

2.1.8	Hardware Interfaces	8

2.1.9	Software Interfaces	9

2.1.10	General Constraints	9

2.1.11	Goals and Guidelines	10

2.1.12	Developmental Methods	11

3	Hardware Design Description	12

3.1	Design Stakeholders	12

3.2	Design Concerns	12

3.2.1	Dow Site Management	12

3.2.2	DTRR Operators	12

3.2.3	NRC	12

3.2.4	DAQ Project Management	12

3.2.5	DAQ Hardware Engineering/Development	12

3.2.6	DAQ Hardware Engineering/Testing	13

4	DAQ Detailed Design	14

4.1	DAQ_IF	14

4.1.1	CPU Interface Board	14

4.1.2	Logic Level Conversion	15

4.1.3	Logic Signal Buffering	17

4.1.4	SPI Chip Select	18

4.1.5	I2C Bus Expansion	18

4.1.6	Application-Defined I/O Pin	20

4.1.7	DAQ_IF Watchdog Timer	20

4.1.8	DAQ_IF Power LED	22

4.1.9	DAQ_IF RS-232	23

4.1.10	PPDO Connection	24

4.1.11	PPDIO96 Connection	25

4.1.12	DAQ_IF Power Supply	25

4.2	PPDIO96 96-bit Parallel I/O Board	27

4.2.1	Capacity and Interface	27

4.2.2	PPDIO96 Bank Connectors	28

4.2.3	PPDIO96 Power Supply	29

4.3	PPOPTO-12 12-Channel Optical Isolation	30

4.3.1	Capacity and Interface	30

4.3.2	Power Supply	30

4.3.3	Signal LEDs	31

4.3.4	Electrical Isolation and Operating Modes	31

4.4	PPSSR-16 16-Channel Solid-State Relay Board	33

4.4.1	Capacity and Interface	33

4.4.2	Power Supply	34

4.4.3	PPSSR-16 Board Select Signal (BS0) and Clocking Data into the PPSSR-16	35

4.4.4	PPSSR-16 Power-On Reset, Watchdog Latch, and the Reset Signal	36

4.4.5	PPSSR-16 Outputs and Output LEDs	41

4.4.6	PPSSR-16 Buffered Signal Lines	43

4.5	PPRELAY-12 12-Channel Mechanical Relay Board	44

4.5.1	Capacity and Interface	44

4.5.2	Power Supply	45

4.5.3	PPRELAY-12 Board Select Signal (BS0) and Clocking Data into the PPRELAY-12	46

4.5.4	PPRELAY-12 Power-On Reset, Watchdog Latch, and the Reset Signal	47

4.5.5	PPRELAY-12 Outputs and Output LEDs	52

4.5.6	PPRELAY-12 Buffered Signal Lines	54

4.6	PPAIO-16/4 16-Channel Analog Input/4-Channel Analog Output Board	55

4.6.1	Capacity, Interface, and Accuracy	55

4.6.2	PPAIO-16/4 I2C Interface, Port Assignment, and Daisy-Chaining	56

4.6.3	PPAIO-16/4 Power Supply	58

4.6.4	PPAIO-16/4 Analog Output Amplifiers	59

4.7	PPAC4 4-Channel Analog Conditioning Board	61

4.7.1	Capacity and Interface	61

4.7.2	PPAC4 Power Supply	62

4.7.3	PPAC4 Isolation Amplifier Section	62

4.7.4	PPAC4 Amplifier Section	63

4.8	PPAC420 8-Channel 4-20 mA Analog Input Conditioning Board	65

4.8.1	Capacity and Interface	65

4.8.2	PPAC420 Power Supply	65

4.9	PPRLYIO-12 12-Channel I/O Relay Board	66

4.9.1	Capacity and Interface	66

4.9.2	PPRLYIO-12 Power Supply	68

4.9.3	PPRLYIO-12 Relay and Data LED Activation	69

Plantation Productions Open Source/Open Hardware Data Acquisition System

HARDWARE DESIGN DESCRIPTION

1	Introduction

This document is the Hardware Design Description (HDD) for the hardware contained in the Digital Data Acquisition System (DAQ) created by Plantation Productions, Inc.

The DAQ system provides digital and analog I/O capabilities for embedded systems; specifically, it was designed to provide data acquisition for TRIGA™ Research Reactors (TRIGA is a registered trademark of General Atomics).

1.1	Purpose

The purpose of this document is to describe the hardware design for the DAQ systeminterfaceDIU.  The intended audiences for this document specificationare the engineering, product assurance and management personnel involved in the hardware development.

1.2	Scope

The scope of the software, which is based on the DAQ Hardware Requirements Specification (DAQ HRS) power failper the requirements that have been allocated to the DAQ system hardware.  From this document the hardware will be developed.

1.3	Contents of the Document

The general description including product perspective, product functions, user characteristics and general constraints is included in Section 2.

The design descriptions are included in Section 3.

The HDD to HRS traceability (reverse traceability) is documented in a separate document (Excel spreadsheet).

1.4	Document Conventions

All tags shall take the form:

<whitespace>	[DAQ_HDD_xxx]

where "xxx" is a three-digit number reserved for HDD usage.

For HDD tags, should the need arise to insert a new HDD tag between two other values (e.g., add a requirement between 030 and 031) then a decimal fractional number shall be appended to the HDD tag number (e.g., 031.5). Any number of decimal point suffixes can be added, if needed (e.g., 030.5.2).

Examples:

From the HDD:

<whitespace>	[DAQ_HDD_053]

Note: because an external script may be used to extract requirements from this document, it is very important that actual requirements in this document begin on a new line (with nothing but white space preceding the requirement) and that the requirement take exactly the form shown above. The regular expression used by the requirement extraction script is the following:

<whitespace>*  '[DAQ_HDD_'  {0-9}{0-9}{0-9}('.' {0-9}+)* ']' <whitespace>* ':' <whitespace>*  .*  '\n'

Where ".*" represents an arbitrary sequence of characters not including a new line and "<whitespace>*" represents zero or more tab or space characters. The actual string "<whitespace>" appears in front of the examples in this section so that they will not be captured by this script; the string "<whitespace>" should not appear in front of actual requirements (though actual whitespace is certainly permissible).

2

Hardware Architecture

The DAQ digital data acquisition system (Hereafter, "DAQ") consists of several main components:

1.	DAQ_IF (DAQ interface board). This circuit board interfaces to a single-board computer such as a Netburner MOD54415 Evaluation Board, a Raspberry Pi 3 Model B, or a Teensy 3.2.

2.	PPDIO96 (96-input digital I/O board). This board connects to the PPDIO96 bus connector on the DAQ_IF board and provides 96 digital I/O pins. Up to six PPDIO96 boards can be connected together in a daisy chain off one DAQ_IF board.

3.	PPOPTO-12 (12-channel digital input opto-isolation). This board provides 12 channels of digital opto-isolation. This board connects to one of the 12-input bank connectors on the PPDIO96. Up to eight PPOPTO-12 boards can be connected to a single PPDIO96 board providing 96 opto-isolated inputs.

4.	PPBreakout (12-channel breakout board for PPDIO96). This board connects to one of the 12-input bank connectors on the PPDIO96. It provides 12 sets of two-terminal screw terminals for the 12 I/O pins on that PPDIO96 bank. The PPBreakout board is useful when feeding inputs to the PPDIO96 that do not require isolation or for connecting digital outputs from the PPDIO96 to the rest of the system.

5.	PPRELAY-12 (12-channel mechanical relay). this board connects to the PPDO bus connector on the DAQ_IF board and provides 12 mechanical relay digital outputs (with NC/NO terminals). In addition, for digital I/O pins capable of sinking up to 150 mA are also available. In theory, an unlimited number of these boards (and PPSSR-16 boards) can be daisy-chained off the PPDO connector. In practice, fan-out limits the system to 10 or fewer boards.

6.	PPSSR-16 (16-channel Solid-State Relay). This board connects to the PPDO bus connector on the DAQ_IF board (or daisy-chains with other PPSSR-16 and PPRELAY-12 boards). It provides 16 solid-state relay controlled outputs. In theory, an unlimited number of these boards (and PPRELAY-12 boards) can be daisy-chained off the PPDO connector. In practice, fan-out limits the system to 10 or fewer boards.

7.	PPAIO-16/4 (16 analog inputs, 4 analog outputs). This board connects to one of the four 6-pin I2C connectors on the DAQ_IF board and provides 16 single-ended 16-bit analog inputs (or 8 double-ended inputs) and four 12-bit analog outputs. The analog inputs support up to a 0-5V range (with programmable gain amplifiers allowing the full-range input of smaller signals). The analog outputs include amplifier circuitry to support outputs in the range -10V to +10V (easily programmable as -5V to +5V, if desired).

8.	PPAC4 (4-channel analog conditioning). This board provides analog isolation and conditioning. The four inputs to this board are single-ended analog signals in the range -10 to +10V. The four outputs from this board are double-ended analog signals (0-4.096V) that provide a full 16-bit range to the PPAIO-16/4 analog inputs. This board also contains isolation amplifiers that isolate the double-ended output from the single-ended input signal.

9.	PPAC420 (8-channel 4-20mA analog conditioning). This board accepts 4-20 mA current loop inputs and produces a single-ended -1.25 to +5V output. Typically, this outputs would be fed as inputs to the PPAC4 (to provide isolation and full-range ADC conversion), though if isolation is not required the inputs could be fed directly into the single-ended inputs on the PPAIO-16/4 board.

2.1	Design Considerations

2.1.1	Assumptions and Dependencies

In the most common use case, the DAQ system will be connected to some host computer via Ethernet, USB, or RS-232 Serial. While it is possible for the DAQ system to operate at a stand-alone data acquisition system, such usage will be rare.

2.1.2	Related Software or Hardware

When running with a Netburner MOD54415 module, the system will be running the µC/OS real-time operating system. When running on a Raspberry Pi, the system will likely be running a variant of the Linux operating system. When running with a Teensy 3.2 module, the software will (likely) be using the Arduino-style library modules provided for the Teensy 3.2.

Because the DAQ system operates using I2C and SPI interfaces, it is quite possible to hook up other I2C and SPI devices. This document will not consider such related hardware.

2.1.3	End-User Characteristics

There are three types of "end-users" associated with the DAQ system: system end users, technicians, and system designers.

System end users (those individual using the final system) may not even be aware of the DAQ system – they are only interested in using the system as a whole and the DAQ system might be a small or hidden part of that whole system.

Technicians are those individuals responsible for maintaining and calibrating the system. Their responsibilities will likely include maintaining and calibrating the components of the DAQ system. As such, they are likely to be concerned with the electronic design and operation of the DAQ system boards.

System designers are those indivduals who design a system around the DAQ system. Clearly, they will require the most knowledge and experience with the DAQ system hardware.

2.1.4	System Interfaces

The DAQ system provides for up to three system interfaces (depending on the computer module controlling the DAQ_IF board): Ethernet (Netburner and Raspberry Pi), USB (Teensy 3.2), and RS-232 (Netburner, Raspberry Pi, and Teensy 3.2).

2.1.5	Fail-Safe

The DAQ system operates in a fail-safe fashion. After a power on restart the PPDIO96 comes up with all the pins programmed as inputs; the PPRELAY-12 and PPSSR-16 digital output boards come up with all the relays turned off (NC in the "C" state, NO in the "O" state, and solid-state relays in the high-impedance state).

The DAQ-IF includes a watch-dog timer that trips a relay if it is not refreshed within 5-10 seconds. If the firmware on the CPU module hangs up or otherwise fails to refresh the watchdog timer within the specified amount of time, a relay will be actuated. The NC/NO outputs from this relay are available for use in the rest of the system (application-defined) to handle the software anamoly. In addition, this signal also appears on the PPDIO96 and PPDO busses. Activation of this signal will place the PPDIO96, PPRELAY-12, and PPSSR-16 boards in the fail-safe state.

Finally, a software programmable line (reset) appearing on the PPDIO96 and PPDO busses will also put the boards into their fail-safe state. Note that the reset line will also reset the watchdog timer if it has expired.

The DAQ_IF board uses a separate digital output line from the CPU module to refresh the watchdog timer. The CPU module must pulse this line (low-to-high edge) at least once every timeout period to keep the watchdog timer from timing out. Note that the watchdog timer is a hardware (RC-based) circuit, it does not depend on software to produce a watchdog timeout.

When designing an end-system around the DAQ system, you should carefully consider the fail-safe design of the DAQ system and wire up any safety-critical systems in an appropriate fashion (e.g., SCRAM loops in a nuclear power reactor).

2.1.6	Hardware Basis

The DAQ hardware is based the data acquisition needs commonly found in TRIGA™ Research Reactors. The design considered the maximum data acquisition requirements for the most complex reactor in existence and then tripled or quadrupled those requirements (in terms of input and output channels) and that became the basis for the design. Because of the generous requirements (up to 576 digital inputs [or outputs], up to 160 relay-controlled outputs, up to 128 analog inputs, and up to 32 analog outputs) the DAQ system should be more than capable for the vast majority of data acquisition projects someone could come up with.

2.1.7	User Interfaces

This document assumes that the DAQ system will be controlled by some host PC. As such, most of the user interface design associated with the DAQ system will occur on the host PC. However, certain user-interface components are present on the DAQ hardware. In particular, all boards will contain a power LED indication power applied to the board (or not). Furthermore, most digital I/O devices provide LEDs for each bit of digital I/O indicating whether the digital I/O pin is active or inactive.

2.1.8	Hardware Interfaces

The DAQ system provides several hardware interfaces to external (to the DAQ) components and systems. As noted earlier, the DAQ system provides Ethernet, USB, and RS-232 interfaces to host computer systems. On the hardware side there are also interfaces to digital inputs, interfaces to digital outputs, interfaces to analog inputs, interfaces to analog outputs, and interfaces to other modules using the I2C and SPI busses.

2.1.8.1	Ethernet Interfaces

The Netburner and Raspberry Pi 3 Model B single-board computers (SBCs) both provide on-board Ethernet interfaces. These SBCs both contain an operating system with a full TCP/IP stack allowing easy communication across the Ethernet using standard socket communications.

The Teensy 3.2 module does not have a built-in Ethernet interface. However, it is possible to purchase an SPI-based Ethernet interface and wire it to the SPI bus (PPDIO96 bus) on the DAQ_IF interface board if Ethernet access is desired when using a Teensy 3.2 SBC. Note, however, that such connections are beyond the scope of this document.

2.1.8.2	USB Interfaces

The Teensy 3.2 SBC includes a small micro-USB connector. You may connect the DAQ_IF board (with Teensy 3.2 installed) to a host computer using a USB-to-micro-USB cable. To the host computer, the Teensy 3.2 looks like a really fast COM port.

In theory, the Netburner can also be programmed to act as a USB device. This document will not consider that option.

The Raspberry Pi 3, while it supports USB, cannot be used as a USB device (it's a USB host). Newer Raspberry Pi Zero units can be programmed as a device (using USB On-the-go) but this document will not consider that option.

2.1.9	Software Interfaces

There are software libraries available for the Teensy 3.2 and Raspberry Pi 3 Model B SBCs that allow you to easily program all the I/O chips in the DAQ system. However, the main software written to support the DAQ system runs on the Netburner MOD54415 Evaluation board plugged into the DAQ_IF board. The software interface for this system is completely described in the SRS (Software Requirements Specification), SDD (Software Design Description), and DAQ Operations manual.

2.1.10	General Constraints

·	Hardware or software environment – The majority of the software is written in the C/C++ programming language.  In addition, there are various "make" files and system scripts used to build or run the system.  Some test software is written in C++ running on the Teensy 3.2 or Raspberry Pi, but the majority of the system code runs under µC/OS on the Netburner.

·	The software is developed under Windows using the Netburner software development kit and software development tools.

·	Availability or volatility of resources – Run within the confines of the Netburner MOD54415 hardware.

·	Interface/Protocol Requirements – The basic intertask communication will be handled by Ethernet socket communications.

·	Data repository and distribution requirements – In a preemptive multitasking operating system, shared data objects must be protected to insure all access is serialized. Typically, this is done with semaphores, mutexes, or critical sections. To provide the necessary data access protection for globals, the code will include a global semaphore to be used by most tasks. This method will insure serialized data access.

·	Memory and other capacity limitations -  There will be no memory constraints other than the total amount of system RAM installed MOD54415 module.  As the software runs on µC/OS, the system limitations 64 MB RAM and 2 MB Flash/ROM.

·	Performance Requirements – The system shall perform all necessary tasks well within the performance capabilities of the MOD54415. During normal operations, all normal I/O and user interface tasks much be completely in less than 25% of the CPU cycles available. Occasional exceptions, lasting no more than a few seconds (less than the DAQ_IF watchdog timeout period), are acceptable as long as these events are infrequent.

·	Network Communications – The system shall use TCP/IP Ethernet communications protocols to communicate between the DAQ system and other devices.

·	Testing – Testing will follow the standard Plantation Productions, Inc., practices for testing systems, as defined by the HTP (Hardware test procedures) and STP (Software Test Procedures) documents.

·	Environmental -- The software shall perform properly while the unit is operating within the environmental constraints for the hardware.

2.1.10.1	Operating System

The DAQ software will utilize the µC/OS pre-emptive priority-based multitasking operating system kernel for microprocessors.  µC/OS was not developed by Plantation Productions, Inc., and may be considered Software of Unknown Provenance (SOUP). However, µC/OS is open-source and its implementation on the Netburner modules has a long history so there is a high confidence in the reliability of this software.

The host computers contain their own software. As the software for those devices is outside the scope of this document, it shall not be considered here.

2.1.10.2	Criticality of the Application

The hardware may be used as part of a research reactor. The hardware's design allows the support of safety critical systems with an appropriate verification and validation (V&V) process in place.

2.1.10.3	Personnel Safety and Security Considerations

The hardware must be designed to protect the safetysafety of personnel who use and maintain it.

2.1.11	Goals and Guidelines

Basic hardware goals:

The hardware is designed to operate as programmed under normal circumstances. In anamolous situations (power up, software hang) the hardware shall enter a special fail-safe mode in which all digital I/O ports that are programmable as digital inputs or outputs revert to inputs and all strict digital output ports are programmed in the "off" (or "open") state. To fully realize this in a system, the following guidelines apply:

1.	The PPDIO96 board should be programmed as input only. Although the system will automatically reset the I/O expander chips to input pins on a reset or watchdog timeout condition, keep in mind that if the pins are actually used as outputs the pins will be floating at that point and won't be in a guaranteed (fail-safe) state immediately after the reset or timeout.

2.	Before writing to a digital output board (PPRELAY-12 or PPSSR-16) the system software should first verify that a watchdog timeout has not occurred (which will force all the outputs to "off" or "open"). If a timeout has occurred, then the system should reinitialize all the digital outputs to some reasonable state.

2.1.12	Developmental Methods

The developmental method used to design the DAQ system hardware was based loosely on the Prototype/Iterative Model. In this Model, being a process, the following phases were followed in order:

1.	Requirements Specification

2.	Hardware Design

3.	Circuit board creation and assembly

4.	Testing (validation)

5.	Repeat steps 1-4 for each new feature or site port.

3

Hardware Design Description

3.1	Design Stakeholders

The initial design of the DAQ system hardware was to support the data acquisition requirements for the Dow TRIGA Research Reactor (DTRR) at Dow Chemical in Midland Michigan. For this project, the project stakeholders are the following:

·	Dow Chemical (site management)

·	Dow Chemical (site operators/users)

·	NRC

·	Plantation Productions, Inc.,  project management

·	Plantation Productions, Inc.,  software engineering/development

·	Plantation Productions, Inc.,  hardware engineering/development

·	Faircloth Engineering (systems hardware engineering development)

·	Plantation Productions, Inc., software quality assurance

Although this design was originally created for DTRR and Dow Chemical, the design is sufficiently generic to be adopted for a wide variety of embedded applications. As such, the stakeholders can easily be swapped for more stakeholders more pertinent to a given application.

3.2	Design Concerns

3.2.1	Dow Site Management

The DAQ design shall provide like-for-like functionality of the existing data acquisition system for DTRR.

3.2.2	DTRR Operators

The console design shall provide a reasonable approximation of the legacy QNX console to reduce the learning curve. This is achieved by providing the like-for-like functionality of the existing console using a similar user interface. In particular, the DAQ system will provide a transparent replacement for obsolete ISA-bus analog and digital I/O boards.

3.2.3	NRC

The DAQ shall follow software quality assurance requirements for research reactors as specified by ANSI 15.15-1978.

3.2.4	DAQ Project Management

The design shall allow implementation, testing, and deployment of the console on schedule and under budget

3.2.5	DAQ Hardware Engineering/Development

The hardware engineering team shall have the following design concerns:

·	The design shall provide the functionality required by the SOW, SyRS, and HRS.

·	The design shall be efficient in terms of space, power usage, and functionality.

·	The design and implementation shall be reliable.

·	The design and implementation shall be maintainable.

3.2.6	DAQ Hardware Engineering/Testing

The hardware testing team shall have the following design concerns:

·	The design shall produce an appropriate set of test cases.

·	The design and hardware shall be such that the system is easy to test.

4	DAQ Detailed Design

4.1	DAQ_IF

4.1.1	CPU Interface Board

1:	[DAQ_HDD_001]

The original DAQ system design was created using a Netburner MOD54415 Evaluation Board as the controlling computer module. However, to make the design slightly more generic and open up the application domain a bit, the design should also include support for other CPU board modules. In the initial design, this should include at least the following modules:

·	A Linux-based CPU module (Raspberry Pi 3 Model B was chosen)

·	An Arduitno-based CPU module (Teensy 3.2 was chosen).

The DAQ_IF board was designed to interface to a CPU module using a single I2C bus, a single SPI bus (and single SPI chip select), and handful of digital I/O pins, and an optional (TTL-level) RS-232 port.

The Netburner MOD54415 Evaluation Board largely defined the signals used by the DAQ_IF (other than RS-232, the MOD54415 Eval Board provides its own RS-232 ports). Pretty much every free available digital I/O line that was available on the MOD54415 Eval board was put to use on the DAQ_IF board. The Raspberry Pi 3's (on its 40-pin GPIO connector) and the Teensy 3.2's I/O pins were mapped to provide this same functionality. The Raspberry Pi and Teensy modules also had TTL-level serial port signals that the DAQ-IF uses for serial communication (note that the DAQ_IF board provides level conversion to RS-232 signals).

In theory, there is no reason one couldn't connect a different computer system to the DAQ_IF board by wiring appropriate signals to the Netburner, Raspberry Pi, or Teensy 3.2 connections on the DAQ_IF board. The only thing to note is that the Netburner, Pi, and Teensy Note that the Teensy 3.2 is 5V tolerant, but is a 3.3V processor. The DAQ_IF interface board uses 3.3V signals when connected to a Teensy 3.2. modules are all 3.3V logic levels so any system connecting to those pins must also support 3.3V logic levels.

Pins in use by the Single-Board Computer interface. All signals are 3.3V logic signals.

| Netburner | Raspberry Pi | Teensy 3.2 | Function |
| --- | --- | --- | --- |
| 15 | 22 | 17 | Output: Watchdog refresh |
| 25 | 23 | 13 | Output: SPI Clock |
| 26 | 29 | 14 | Output: A0 (SPI chip select L.O. bit) |
| 27 | 21 | 12 | Input: MISO (SPI data in) |
| 28 | 19 | 11 | Output: MOSI (SPI data out) |
| 30 | 24 | 10 | Output: SPI CS (SPI master chip select) |
| 34 | 31 | 15 | Output: A1 (SPI chip select middle bit) |
| 36 | 33 | 16 | Output: A2 (SPI chip select H.O. bit) |
| 38 | 37 | 21 | I/O: Reserved for future expansion |
| 39 | 3 | 18 | I/O: I2C data line |
| 41 | 32 | 20 | Input: WD timeout latch input |
| 42 | 5 | 19 | I/O: I2C clock line |
| 44 | 16 | 23 | Output: Reset (DAQ hardware) |
| 48 | 18 | 22 | Input: IRQ (Interrupt Request) |
| xx | 8 | 1 | Output: TDX1 (RS-232 transmit) |
| xx | 10 | 0 | Input: RDX1 (RS-232 receive) |
| xx | 11 | 2 | Input; RTS1 (RS-232 request to send) |
| xx | 36 | 3 | Output: CTS1 (RS-232 clear to send) |

4.1.2	Logic Level Conversion

2:	[DAQ_HDD_002]

All of the DAQ system modules except the CPU interface operate using TTL/5V logic level signals. Therefore, all the 3.3V signals on the CPU lines must be translated to 5V signals for the rest of the system.

For the non-I2C signals, an Adafruit TXB0108 breakout board provides appropriate level conversion between 3.3V and 5V logic signals. The TXB0108 IC is a surface-mount device (SMD). One design rule for the DAQ system is to use through-hole parts and avoid SMDs and system maintenance and trouble-shooting is much more difficult when using SMDs. Breakout boards provide a solution when only SMDs are available for a given function. Breakout boards are small circuit boards containing SMD circuitry that bring out the pins on the surface mount devices to 0.1" header pins. The DAQ system treats these breakout boards like any other IC. In the case of the TXB0108 IC, Adafruit provides a small 20-pin breakout board  that contains the TXB0108, decoupling capacitors, and a resistor all in the same package. It is very easy to connect test leads to the pins and if the device is damaged, you can replace the whole breakout board and not worry about having to desolder and solder SMD parts on the DAQ_IF board.

The TXB0108 board provides an array of eight bi-directional level shifter circuits. The DAQ_IF board uses seven of these circuits (leaving one free for future use). These signals are the following:

·	MOSI (SPI data output)

·	MISO (SPI data input)

·	SPI CLK (SPI clock output)

·	IRQ (interrupt request input)

·	J2_38 (Spare I/O line, input/output)

·	WD_Latch (Watchdog latch input)

Because of the open-collector nature of the I2C the I2C signals cannot pass through the TXB0108 IC. Adafruit makes a specialized I2C level-shifting breakout board, the BSS138 that uses a set of BSS132 Field-Effect Transistors (FETs) to to level shifting for the I2C bus. The SCL and SDA lines from the CPU interface pass through this level shifter.

The reset line is a special case. This is an output line from the CPU interface that instructs all the hardware modules to reset/initialize themselves and enter a fail-safe condition. The DAQ_IF board needs to pass this signal to an I2C multiplexer (TCA9585 breakout board, also on the DAQ_IF). However, this I2C breakout board has a pull-up resistor attached to this line. Pull-up resistors play havoc with the BX0108 level shifter chip so connecting the RST pin on the TCA9584 breakout board directly to the 5V side of the TXB0108 will force the reset pin constantly high (meaning you can never reset anything in the system with this pin).

To solve this problem, the (3.3V) reset signal is fed into a transistor pair (the second transistor exists simply to invert the inverted signal from the first transistor) and use that as a switch to pull the RST pin on the I2C  multiplexer low when the reset signal is active (also low).

4.1.3	Logic Signal Buffering

3:	[DAQ_HDD_003]

The DAQ_IF board transmits several of the digital signals it produces along the PPDO and PPDIO96 busses. A system designer can connect up to six PPDIO96 (or other SPI interfaces) to the PPDIO96 bus and a virtually unlimited number of PPRELAY or PPSSR (or other SPI interfaces) to the PPDO bus. Even if each board in the daisy-chain presents only one TTL load on this signals, the fanout could quickly render the signals unreliable and noisy.

To solve this problem, the DAQ_IF board includes a 74HC244 (dual 4-channel buffer) IC to provide buffering for the following signals:

·	MOSI (SPI output )

·	SPK CLK

·	RESET

·	WD_Latch

The DAQ_IF board actually produces two copies of each of these signals. One buffered copy is provided on the PPDIO96 bus and the second buffered copy is placed on the PPDO bus. The 74HC255 chip supports the equivalent of 15 TTL loads on each of these two busses. As long as the boards attached to these busses present only 1 TTL load each (as specified by the hardware requirements) one could, in theory, attach up to 15 boards to each bus. In practice, the PPDIO96 bus is limited to 6 boards due to the number of SPI chip select lines present on the bus and the PPDO bus is probably limited to around 10 boards due to cable capacitance and other issues.

4.1.4	SPI Chip Select

4:	[DAQ_HDD_004]

The DAQ_IF hardware requirements assume that there is a single SPI CS (chip select) line available from the CPU module (this could be a hard-wired SPI chip select line that is automatically handled by the on-board SPI hardware or a generic digital output line that is programmed via software). In addition to this chip select line, the DAQ_IF expects three software-programmable output lines that can be decoded to produce eight separate SPI chip select lines.

The DAQ_IF circuit labels the three software-driven chip select lines A0, A1, and A3. These form a 3-bit binary number producing a chip select value of 0 through 7. Connecting these lines to a 3-to-8 decoder (e.g., 74hc138) produces eight chip select lines (labeled BS0-BS7 for board select zero through board select seven). The actual SPI chip select line (usually handled by hardware) is used as one of the decoder/demultiplexer enable inputs.

The BS0 (board select zero) signal controls the PPDO bus. Boards attached to the PPDO bus (e.g., PPRELAY-12 and PPSSR-16) operate in a serial shift register fashion. That is, bits are shifted into the first board in the PPDO daisy chain and the previous bits from the first board are shifted to the second board; the previous bits from the second board are shifted to the third, etc. As such, only a single SPI chip select line is necessary to control any number of PPDO boards.

The BS1 through BS6 lines connect to the PPDIO96 bus connector.  These six SPI chip select lines allow a system designer to connect six PPDIO96 boards (or other SPI devices) to the PPDIO96 bus.

The BS7 chip select line is intentionally left disconnected. The intent is to program the decoder with A0, A1, A2 equal to (1, 1, 1) whenever none of the other seven chip selects are active. Note that this convention is redundant – if the SPI-CS line is not active (low) then none of the BSn lines will be active (low).

4.1.5	I2C Bus Expansion

5:	[DAQ_HDD_005]

The DAQ_IF uses an Adafruit TCA9584 breakout board to provide I2C expansion. The single I2C bus provided by the CPU module is fed into the TCA9584 to produce eight separate I2C busses. The TCA9584 IC consumes a single address in the I2C address space. Writing a byte to this I2C address with a single bit set activates the corresponding I2C bus on the TCA9584 until a different value is written to that address. On the DAQ_IF, that magic address is 0x70 (obtained by wiring the three address lines on the TCA9584 breakout board to ground).

On power up, or whenever the I2CRESET signal is pulsed (low), the TCA9584 initializes to "no busses selected. Writing a zero to I2C address 0x70 also disables all busses. Note that the DAQ_IF hardware includes a four-pin header with I2C signals (plus Vcc and Gnd) that is always active (as it sits before the TCA9584 breakout board).

Unlike the SPI bus and certain other signals, the DAQ_F does not buffer the I2C bus signals. This is because (when using the PPAIO-16/4 boards) there aren't that many (TTL) loads placed on each I2C bus. However, if you connect other devices to the eight expansion I2C busses be aware of the fanout issues.

The DAQ_IF board routes the eight expansion I2C busses to a set of four six-pin headers. These headers have the following pin out:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | SDAn | 2 | SDAn+1 |
| 3 | SCLn | 4 | SCLn+1 |
| 5 | Gnd | 6 | Gnd |

Each six-pin header comprises two I2C busses. The odd-numbered pins make up the first bus, the even-numbered pins make up the second bus. Between the four connectors, there are a total of eight I2C busses:

In a typical DAQ system setup, the PPAIO-16/4 boards connect to the I2C expansion busses. You may daisy-chain two PPAIO-16/4 boards on the same bus. The first PPAIO-16/4 uses the first I2C bus for its ADC modules, the second ADC module uses the second I2C bus for its modules.

Both PPAIO-16/4 boards use both busses for the DAC modules. The first board will deploy Adafruit MCP4725 DAC modules (I2C addresses 0x62 and 0x63) while the second board will use Sparkfun MCP4725 DAC modules (I2C addresses 0x60 and 0x61).

It would have been possible to have each board utilitize only a single I2C bus by mixing Adafruit and Sparkfun DACs on the same PPAIO-16/4 board. However, the current design allows you to provide up to 16 DACs in the system (and 64 single-ended ADCs) using parts from a single supplier (Adafruit) by using four non-daisy-chained PPAIO-16/4 boards connected to the four I2C bus connectors. You would only have to deal with a second supplier (Sparkfun) if you need ore than 16 DACs in the system.

4.1.6	Application-Defined I/O Pin

6:	[DAQ_HDD_006]

The DAQ_IF board requires a single application-defined I/O pin. This signal will be present on both the PPDO and PPDIO96 busses. The signal is named "J2_38" (the name comes from the fact that this is pin 38 on the J2 connector of the Netburner MOD54415 Evaluation Board; obviously this name doesn't have a direct meaning on the Teensy or Pi CPU modules).

This pin is application-defined and may be programmed as an input or an output pin on all CPU modules. Note that this pin does not run through a buffer, so there is a limit to the number of inputs (TTL loads) it can drive on the busses when being used as an output pin.

4.1.7	DAQ_IF Watchdog Timer

7:	[DAQ_HDD_007]

The DAQ_IF board provides a watchdog timer circuit with latching relay.

The watchdog timeout is provided by a Toshiba TA8030S watchdog timer chip. This chip produces an active low signal on the RST1 pin whenever a power on condition occurs or whenever a timeout period occurs. The timeout period is specified by the RC time constant obtained from R1 and C6 in the above schematic (100K * 50 µC is approximately 5 seconds plus or minus the accuracy of the RC components). The requirements state that the watchdog timeout period is a minimum of two seconds and a maximum of ten seconds. This RC circuit safely implements that timeout period.

The TA8030S documentation states that maximum width of the reset pulse is 0.6*R1*C6 in the circuit above. This implies that the RST1 signal could be held low for as long as three seconds (nominally) after a watchdog timeout period.  As this signal drives the preset lines on a pair of 74HC74 flip-flops (the watchdog timeout latches), this means that the system should not attempt to reset (clear) the watchdog latches until the RST1 circuit goes high. There is no input to the system (software) telling it that this signal is no longer active. Therefore, whenever the system sees that the WD_LATCH signal is active (this is the WD_LATCH_5 signal coming from the second 74HC74 flip-flop above), the system should wait five seconds before attempting to reset the watchdog latches.

The system resets the watchdog latches by sending an active-low pulse on the RESET output line. Note that activating this signal will also reset all the other boards in the system (this toggles the reset pins on all the MCP23S17 I/O expander chips found on the PPDIO96 boards, it puts the PPRELAY-12 and PPSSR-16 boards into fail-safe mode, and it resets the I2C expander chip on the DAQ_IF board).

In the circuit above, a capacitor appears in series with the RESET signal and the CLR lines on the flip-flops. This prevents an errant always-low signal on the RESET line from constantly clearing the watchdog state on the 74HC74 flip-flops. A pull-up resistor keeps this signal high when it's not being actively pulled low. The combination of the two produces a brief pulse to clear the flip-flops when an active-low signal is first sent.  A zener diode (1N4733A) is added to the circuit to shunt excessively high voltages to ground (this occurs on the rising edge of the reset signal) to protect the inputs on the 74HC74 chip.

The WD_RFSH signal refreshes the TA8030S watchdog timer. The CPU module must pulse this pin (typically a low-to-high-to-low pulse) every two seconds, or faster, to prevent the watchdog timer module from timing out. Note that this pin also drives an LED. The intent is to invert the WD_RFSH at (better than) twice the normal refresh interval (i.e., invert the pin faster than once per second) to obtain a "heartbeat" flashing LED effect.

Note that both halves of the 74HC74 package are provided with the same inputs. One flip-flop produces the WD_LATCH_5 signal which the DAQ_IF passes on to the CPU module and two the PPDO and PPDIO96 busses. The boards on the busses can use this signal to determine that a watchdog failure has occurred (and switch to fail-safe mode, if desired). The CPU can monitor this signal to determine if there has been a watchdog failure (assuming the CPU is still running) and send an appropropriate reset signal after dealing with the fact that there has been a watchdog timeout.

The other flip-flop drives the relay circuit. It goes to a transistor that turns on a relay whenever the watchdog condition is latched. This also illuiminates an LED so a human can see that the WD timeout condition is active. The 1N4148 diode across the relay coil pins is a standard clamping diode used to short high-voltages produced by inductive kick-back across the relay coil.

The NC/NO outputs from the relay are presented on a three-pin connector (NC/COM/NO) and are application-defined. The DAQ_IF board does not use the relay except as a way of signaling external hardware that a timeout has occurred.

4.1.8	DAQ_IF Power LED

8:	[DAQ_HDD_008]

The DAQ_IF board, like most boards in the DAQ system, provides an LED that illuminates whenever power is present on the board.

4.1.9	DAQ_IF RS-232

9:	[DAQ_HDD_009]

The DAQ_IF board provides RS-232 level shifting to take TTL level serial communication signals and amplify them to RS-232 levels. In addition to the level shifting, the DAQ_IF board also provides two DB-9 connectors (male and female, DTE and DCE) to allow connection to standard RS-232 serial devices.

The DAQ_IF board alternately allows connection of the TTL serial signals to an FTDI-compatible header (allowing the connection of an FTDI-compatible USB-to-serial cable) or the connection of a SparkFun "OpenLog" serial logging module. Note that only one of these three options (RS-232 level shifting, FTDI cable, or OpenLog module) may be populated on the board. Installing two or more of these devices would create signal conflicts.

If RS-232 level shifting (to the DB-9 connectors) is desired, then the DAQ_IF should populate the BoB5 socket with a SparkFun MAX3232 breakout board. This breakout board contains a Maxim IC (SMD) that will convert between TTL level signals and RS-232 signals. The MAX3232 breakout board automatically produces the ±12V needed for RS-232 communications without any additional power supplies. Note that the DTE and DCE DB9 connectors are wired in parallel with each other (with appropriate pins swapped). Generally you would only connect to one of these connectors at a time (depending on what you're connecting to). Connectiing active signals to both connectors would create signal conflicts.

When using the Sparkfun MAX3232 breakout board, you must leave the FTDI header and the OpenLog circuits unpopulated.

An alternative to using the DB9 RS-232 connectors is to use the FTDI header. FTDI is a special 6-pin USB-to-serial cable used for microcontroller programming (e.g., many Arduino-type boards use this cable). FTDI cables are very common and relatively inexpensive (typically under $10 US).

When using the FTDI header with an FTDI cable, you must leave the SparkFun MAX3232 and OpenLog sockets unpopulated.

A third alternative is to use a Sparkfun OpenLog module.  This module contains a small CPU and a connection for a flash card to log all data written to the serial port (using the OpenLog protocol). In practice, the OpenLog only makes sense when using the Teensy 3.2 CPU module. On the Raspberry Pi you (presumably) have lots of Flash storage to write log files to. The Netburner module cannot access the serial facilities on the DAQ_IF (the Netburner has its own serial ports and doesn't use those on the DAQ_IF).

When using the OpenLog header on the DAQ_IF, you must leave the SparkFun MAX3232 and FTDI sockets unpopulated.

As just noted above, the Netburner MOD54425 Evaluation board has two (level-shifted) RS-232 ports present on the eval board itself. Therefore, RS-232 communications take place directly on the Netburner board itself, those signals are not routed to the DAQ_IF circuitry.

4.1.10	PPDO Connection

10:	[DAQ_HDD_010]

The PPDO bus on the DAQ_IF board is a 10-pin header (2x5) with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Output: BS0 (SPI Chip Select) | 2 | Vcc |
| 3 | Input: MISO (SPI input) | 4 | Output: MOSI (SPI output) |
| 5 | Output: SPI Clk | 6 | I/O: J2_38 |
| 7 | Output: RESET | 8 | Output: WD_LATCH |
| 9 | Input: IRQ | 10 | Gnd |

The PPDO bus is intended for use by the PPRELAY-12 and PPSSR-16 boards. Note that these boards do not use the IRQ, J2_38, and MISO signals (the boards do not have any need for interrupt capabilities, hence no IRQ support; J2_38 is reserved for end-user applications, and these board are strictly output boards so there is no need for the MISO signal). However, these signals are included for future expansion on the PPDO bus.

All signals on the PPDO bus are 5V logic signals having passed through the Adafruit TXB0108 bi-directional level shifter. Futhermore, the MOSI, SPI-Clk, Reset, and WD_Latch signals are also buffered via a 74HC244 dual quad non-inverting buffer chip,

4.1.11	PPDIO96 Connection

11:	[DAQ_HDD_011]

The PPDIO96 bus on the DAQ_IF board is a 14-pin header (2x7) with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | I/O: J2_38 | 2 | Output: WD_LATCH |
| 3 | Output: BS1 | 4 | Gnd |
| 5 | Output: BS2 | 6 | Output: MOSI (SPI data out) |
| 7 | Output: BS3 | 8 | Output: SPI Clk |
| 9 | Output: BS4 | 10 | Input: MISO (SPI data in) |
| 11 | Output: BS5 | 12 | Input: IRQ |
| 13 | Output: BS6 | 14 | Output: Reset |

All signals on the PPDIO96 bus connector are 5V logical signals. The MOSI, SPI Clk, WD_Latch, and Reset signals are also buffered (independently of the same signals on the PPDO connector). The BSn signals are not buffered, but as they are intended for consumption by a singla PPDIO96 board, this shouldn't be a problem; however, if you connect a different board (or many boards) with many TTL loads to one of these signals, you should consider buffering them on that board(s).

4.1.12	DAQ_IF Power Supply

12:	[DAQ_HDD_012]

The DAQ_IF board shall use a single +5V power supply that connects to the board via a screw-terminal module with two terminals (+5V and Gnd).  Application of power to this power supply jack will illuminate the power on LED on the board. Because several components on the board require 3.3V in addition to the components that require 5V, the DAQ_IF board provides a 3.3V voltage regulator circuit:

The 3.3V regulator does not provide power to the Teensy 3.2, Raspberry Pi, or Netburner modules (all of which require far more power than the LD1117v33 regulator can provide). The Teensy 3.2 gets its power from the +5V supply, the Pi and Netburner modules have separate power supply inputs. On the DAQ_IF board, the 3.3V supply is largely used for the level shifters.

4.2	PPDIO96 96-bit Parallel I/O Board

4.2.1	Capacity and Interface

13:	[DAQ_HDD_013]

The PPDIO96 parallel I/O board provides 96 bits of general-purpose digital I/O using six MCP23S17 GPIO expander ICs (16 bits of I/O per IC). The 96 bits are brought out to eight 20-pin (2x10) headers. The PPDIO96 board also connects eight of the I/O lines (bits 88-95) to an eight-position DIP switch. If these switches are in the open position then it is possible to read the data on the associated 20-pin connector. If the software is actually reading these switches there should be no external hardware connected to D88 through D95. Note that the use of these dip switches assumes that the software has programmed the internal pull-up resistors for these bits inside the MCP23S17 IC.

There are two 14-pin headers on the PPDIO96 board that handle data transmission to the DAQ_IF and to other, daisy-chained PPDIO96 boards. One 14-pin header is the input connector (that has the same pinout as the PPDIO96 bus connector on the DAQ_IF board), the second is the output connector that connects to daisy-chained PPDIO96 boards. The input connector has the following pin out (same as the PPDIO96 header on the DAQ_IF):

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | I/O: J2_38 | 2 | Output: WD_LATCH |
| 3 | Output: BS1 | 4 | Gnd |
| 5 | Output: BS2 | 6 | Output: MOSI (SPI data out) |
| 7 | Output: BS3 | 8 | Output: SPI Clk |
| 9 | Output: BS4 | 10 | Input: MISO (SPI data in) |
| 11 | Output: BS5 | 12 | Input: IRQ |
| 13 | Output: BS6 | 14 | Output: Reset |

With one (big) exception, the PPDIO96 board passes all the signals on the input PPDIO96 input connector straight through to the output connector. The exception is how it passes the board select lines (BSn) to the following PPDIO96 board in the chain. On output, the board routes the BS2 input to the BS1 output, the BS3 input to the BS2 output, …, and the BS6 output to the BS5 output. BS1 on the input side does not appear on the output connector. BS6 on the output side is tied to Vcc (meaning "never selected").

The PPDIO96 board also buffers all incoming signals it uses (except BS1, because the assumption is that no other boards in the chain will have access to BS1 as it is not passed through to the output connector). These signals include MOSI, SPI Clk, MISO, and Reset. Note that the board does not use the WD_Latch or J2_38 signals, so it doesn't bother buffering these. IRQ is assume to be an open collector/open drain circuit (with a pull-up resistor) so it doesn't bother buffering this signal, either.

Note that the buffer ICs are 74HC125 devices (quad tri-state buffers) whose buffer signals are only active while BS1 is active (low). For the MISO line (input to the DAQ_IF board) these keeps multiple PPDIO96 boards from interfering with one another.

Because of the buffering, the DAQ_IF only presents one TTL load on the buffered signal lines. This allows the daisy-chaining of up to six PPDIO96 boards on the bus without having to worry about logic level drive and fanout problems.

The PPDIO96 board allows the connection of the IRQ pin on each of the MCP23S17 ICs to the IRQ bus by installing a jumper block on the INTA header associated with each chip.

4.2.2	PPDIO96 Bank Connectors

14:	[DAQ_HDD_014]

The PPDIO96 parallel I/O board has eight 20-pin connectors labeled "Bank 0" through "Bank 7". These connectors each have the following pinout:

| PPDIO96 Bank Pinout for Bank headers 0-7 |
| --- |
| D(1+bank*8) is the data line for bank = 0 through 7 |
| Pin | Description | Pin | Description |
| 1 | D(1+bank*12), e.g., D1 for bank 0 | 2 | D(0+bank*12), e.g., D0 for bank 0 |
| 3 | D(2+bank*12), e.g., D2 for bank 0 | 4 | Gnd |
| 5 | D(3+bank*12), e.g., D3 for bank 0 | 6 | Gnd |
| 7 | D(4+bank*12), e.g., D4 for bank 0 | 8 | Gnd |
| 9 | D(5+bank*12), e.g., D5 for bank 0 | 10 | Gnd |
| 11 | D(6+bank*12), e.g., D6 for bank 0 | 12 | Gnd |
| 13 | D(7+bank*12), e.g., D7 for bank 0 | 14 | Gnd |
| 15 | D(8+bank*12), e.g., D8 for bank 0 | 16 | Gnd |
| 17 | D(9+bank*12), e.g., D9 for bank 0 | 18 | Gnd |
| 19 | D(10+bank*12), e.g., D10 for bank 0 | 20 | D(11+bank*12), e.g., D11 for bank 0 |

In the table above, the particular bit number on a bank is computed by a bit number in the range 0..11 plus the bank number times 12

In order to fit four bank headers across the length of the board, the headers only provide 8 (common) ground pins rather than the 12 ground pins one would normally expect on such a header. The MCP23S17 does not source or sink much current per pin and the signals are not isolated from one another, so having separate ground pins isn't (electrically) necessary. By using only 8 ground pins, the bank header requires only 20 pins rather than 24, saving board space.  Eight ground pins is certainly sufficient for the small amount of current 12 pins from the MCP23S17 will carry.

4.2.3	PPDIO96 Power Supply

15:	[DAQ_HDD_015]

The PPDIO96 parallel I/O board runs off a +5V power supply. As with most DAQ system boards, the PPDIO96 board illuminates an LED when power is applied to the board.

4.3	PPOPTO-12 12-Channel Optical Isolation

4.3.1	Capacity and Interface

16:	[DAQ_HDD_016]

The PPOPTO-12 board provides 12 channels of optical isolation for digital input devices. It provides 12 sets of screw terminals (two terminals each) as inputs and a 20-pin (2x10) header that connects to one of the bank headers on the PPDIO96 board. In addition to the 12 screw terminal pairs, the PPOPTO-12 board also provides a 24-pin header (2x12) that allows a ribbon-cable connection as input to the board. Note: Using the ribbon cable interface may reduce isolation as higher-frequency signals may induce noise on other lines on the ribbon cable if it is not properly shielded or is sufficiently long.

Each screw terminal has a positive (signal) and negative (ground) terminal, as indicated on the circuit board. The pinout for the 24-pin header is as follows:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | D0+ in | 2 | D0- in (Gnd) |
| 3 | D1+ in | 4 | D1- in (Gnd) |
| 5 | D2+ in | 6 | D2- in (Gnd) |
| 7 | D3+ in | 8 | D3- in (Gnd) |
| 9 | D4+ in | 10 | D4- in (Gnd) |
| 11 | D5+ in | 12 | D5- in (Gnd) |
| 13 | D6+ in | 14 | D6- in (Gnd) |
| 15 | D7+ in | 16 | D7- in (Gnd) |
| 17 | D8+ in | 18 | D8- in (Gnd) |
| 19 | D9+ in | 20 | D9- in (Gnd) |
| 21 | D10+ in | 22 | D10- in (Gnd) |
| 23 | D11+ in | 24 | D11- in (Gnd) |

4.3.2	Power Supply

17:	[DAQ_HDD_017]

The PPOPTO-12 uses a single +5V power supply that comes in on a two-conductor pair of screw terminals. As for most DAQ system boards, applying power also illuminates an LED indication power on.

4.3.3	Signal LEDs

18:	[DAQ_HDD_018]

Each isolated channel on the PPOPTO-12 provides an LED to indicate whether that channel is active or inactive. The LED is illuminated when the channel is active and the LED is off when the channel is inactive. "Active" means that the input pins are shorted when operating in "dry contact" mode, it means that an appropriate voltage level appears on the Dn+ pin (relative to the Dn- pin, where n is a channel number in the range 0 to 11) when not in "Dry Contact" mode.

4.3.4	Electrical Isolation and Operating Modes

19:	[DAQ_HDD_019]

Each channel on the PPOPTO-12 is isolated from all the other channels as well as being isolated from the digital outputs from the board (i.e., isolated from the PPDIO96 board). Isolation is achieved using two different ICs per channel. First of all, a PS2501-4 optical isolation chip isolates each channel from the rest of the DAQ system (specifically, the PPDIO96 board). Second, an isolation power supply (CRL2S) provides an independent and isolated power supply for each channel (when operating in "Dry Contact" mode).

The PS2501-4 is a quad opto-isolation package with each channel containing an LED (driven by the circuit to be isolated) and photo detector (providing a signal to the isolated system, in this case the PPDIO96 board). When the circuit to be isolated turns the LED on, this creates a low-impedance condition across the photo detector that the DAQ system sees as a switch closure. A typical optical isolation device such as the PS2501-4 offers better than 1000V isolation.

The circuit to be isolated (that is, the input to the PPOPTO-12 channel) must supply an appropriate current-limited voltage to drive the LED inside the PS2501-4 package. If the external circuit produces an appropriate voltage (the specifications allow for voltages in the range 5V to 24V) all that is necessary is an appropriate current limiting resistor in series with the input of the PS2501-4. For 5V inputs, a resistance of approximately 470 Ω. For 10-12V a 1 kΩ resistor suffices. For 15V use a 1.5 kΩ resistor in series with the PS2501-5. And so on for other voltages.

Often, the digital inputs to a system (such as the PPOPTO-12 channels) are "Dry Contact" inputs rather than voltage or logic levels. A dry contact input is something like a switch or relay contact where the signal consists of a shorted pair of input wires or an open pair of input wires. For dry contact inputs the PPOPTO-12 channels provide a +5V power source (though a pull up resistor). The +5V signal, when the dry contact is open, turns on the LED. When the dry contact is shorted, this pulls  the +5V signal to ground, turning off the LED (and putting the photo conductor in a high impedance state).

A 4-pin (2x2) header on each input channel allows you to program that channel for dry contact or voltage level operation. Putting jumper blocks on pins 1-3 and pins 2-4 programs the device for dry contact operation. In this mode, closing the contacts across the D+ and D- inputs will pull the D- Out signal (connected to the PS2501-4 input) to ground, while feeding +5V to the other leg of the LED in the PS2501-4. This turns the LED on (and activates the photo detector). When the D+ and D- inputs are not shorted, +5V is still being fed to the anode of the LED but the cathode leg is floating. Thus the LED is off (and the photo detector goes into high impedance mode).

Putting a jumper block on pins 3-4 (and leaving pins 1-2 open) on the jumper block disconnects the isolated power supply from the circuit and feeds the D+ input signal directly to the anode input of the PS2501-4 LED (the D- input remains connected to the LED's cathode). In this mode, an appropriate positive voltage (relative to D-) turns the LED on.

You will note that there is a 100 Ω (1/2 watt) between the isolated Vcc and Gnd on the CRL2S. This resistor is present because isolated power supplies require at least a 10% load or the output voltage can rise (to almost double the rated output voltage). As the LED doesn't represent much of a load to the power supply, the 100 Ω resistor guarantees that there is at least a 10% load on the circuit. Note that if you're not using the dry contact mode for a particular channel, you can save several dollars by not populating the board with the CRL2S isolated power supply (which isn't especially cheap); this will also reduce power consumption on the board as the 100 Ω resistor won't be acting as a quarter-watt heater in the system.

4.4	PPSSR-16 16-Channel Solid-State Relay Board

4.4.1	Capacity and Interface

20:	[DAQ_HDD_020]

The PPSSR-16 board provides 16 channels of solid-state relay control for digital output devices. It provides 16 sets of screw terminals (two terminals each) as outputs and a pair of 10-pin (2x5) headers that connect to the PPDO connector on the DAQ_IF board and provide a daisy-chain output to another output board.

The PPDO input connector is a 10-pin header (2x5) with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Output: BS0 (SPI Chip Select) | 2 | N/C |
| 3 | Input: MISO (SPI input) | 4 | Output: MOSI (SPI output) |
| 5 | Output: SPI Clk | 6 | I/O: J2_38 |
| 7 | Output: RESET | 8 | Output: WD_LATCH |
| 9 | Input: IRQ | 10 | Gnd |

The PPDO output connector is nearly identical, with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Output: BS0 (SPI Chip Select) | 2 | Vcc |
| 3 | Input: MISO (SPI input) | 4 | Output: MOSI (SPI output) |
| 5 | Output: SPI Clk | 6 | I/O: J2_38 |
| 7 | Output: RESET | 8 | Output: WD_LATCH |
| 9 | Input: IRQ | 10 | Gnd |

The differences are on Pin 2 and pin 4. The input connector (+5V from the previous board in the daisy-chain) is left disconnected on the input connector. Pin 2 is connected to Vcc (+5V) on the output connector. Pin 4 on the input connector is tied to the serial in pin of the first TPIC6B595 serial shift register. Pin 4 on the output connector is tied to the serial out pin of the second TPIC6B595 IC (Serial data flows into the first shift register, out of the first and into the second shift register, and then out of the second shift register and to the output connector).

As the PPSSR-16 board is a digital-output-only board, the PPSR-16 ignores the MISO input pin.

4.4.2	Power Supply

21:	[DAQ_HDD_021]

The PPSSR-16 receives +5V power and ground on a two-pin screw terminal. As with most DAQ system boards, there is an LED connected to the power supply to indicate when power is applied.

The greatest power use on the board will be the current required to actuate the solid-state relays. For the AQZ-10 SSR an LED drives the relay with a maximum forward current of 50 mA (though the maximum turn-on current is 3mA). Therefore, absolute worst case, is 16* 50mA or 800 mA of current to the board.  In reality, there is a 390 Ω resistor in series with the LED, so with a +5V supply expect less than 15 mA per circuit (total 240 mA) if all relays are activated. In addition to the LED inside the SSR, there is an LED associated with each output channel that illuminates whenever the SSR is actuated. These LEDs have a 470 Ω resistor, so each LED will also consume just under 15 mA. Of course, the rest of the board also draws current, so it's not unreasonable to expect upwards of 500 mA to be pulled from the power supply when all relays are actuated.

Note that the power switched by the relays is (theoretically) independent of the power supplied to the board. Unless you are powering some external circuit being switched by the relays from the PPSSR-16's power supply, their power usage doesn't count towards the power used by the board.

4.4.3	PPSSR-16 Board Select Signal (BS0) and Clocking Data into the PPSSR-16

22:	[DAQ_HDD_022]

The PPSSR-16 contains three input signal lines that control shifting data into the TPIC6B595 shift register and transferring that data to the output latches: BS0, SPI-CLK, and MOSI. These three signals correspond to three of the four SPI control lines (CS, SCK, and MOSI; as an output line the fourth SPI control line, MISO, is not used).

Note: although the PPSSR-16 board uses the SPI control lines, the PPSSR-16 isn't, technically speaking, an SPI device. It just so happens that the SPI clock and MOSI lines work fine as inputs to the TPIC6B's shift in and clock inputs. This "grand coincidence" allows the DAQ system to use the SPI bus to control shift-register-based digital output boards (e.g., PPSSR-16 and PPRELAY-12) on the system SPI bus.

To shift data into the two TPIC6B595 shift registers on the PPSSR-16, the system should first switch the BS0 (board select 0) from high to low. The BS0 signal must be held low for the entire shift duration. Note that if you connect multiple PPSSR-16 (and PPRELAY-12) boards in a daisy-chain on a single PPDO bus (i.e., off a single DAQ_IF board) then you must hold BS0 low while shifting out the bits for all boards. For example, if you have three output boards connected in a daisy chain, you need to hold BS0 low while shifting out all 48 bits for the three boards. Although PPRELAY-12 board possess only 12 relays, they are still 16-bit boards. Four of the output bits are sent to a header rather than controlling relays. Therefore, you must shift 16 bits for each board, regardless of whether it is a PPSSR-16 or PPRELAY-12 board.

The TPIC6B595 shift registers shift the data present on the SER_IN pin into the shift register on the rising edge of the SRCK (SPI-CLK) signal. As in turns out, this is the exact waveform you want when transmitting data on the SPI bus. The bit shifted out appears on the SER_OUT pin that you normally feed to the input of any additional TPIC6B595 ICs in the chain.

On the rising edge of the BS0 signal, the PPSSR-16 boards copy the bits in the shift register over to the output latch. To transfer the bits, a rising-edge clock signal must appear on the TPIC6B595 RCK input. The PPSSR16 synthesizes this clock by putting a positive-edge detection circuit on the BS0 input:

On the rising edge of the BS0 signal the transistor momentarily (about 5 µSec = C6 * R35) conducts pulling the RCK signal low for that time period. On the rising edge of that 5 µSec pulse (which occurs at least 5 µSec after BS0 has gone high) the TPIC6B595 shift register copies the data from the input shift register to the output latch.

4.4.4	PPSSR-16 Power-On Reset, Watchdog Latch, and the Reset Signal

23:	[DAQ_HDD_023]

The PPSSR-16 board, by requirement, must enter a "fail-safe mode" whenever power is first applied, whenever there is an explicit reset operation (a low pulse on the reset pin), or whenever the DAQ system has a watchdog timeout (low signal on the WD_LATCH input pin).

A "fail-safe mode" is defined as follows:

·	If no power is applied to the PPSSR-16 board, the solid-state relays remain in a high-impedance (non-conducting) state. This state is guaranteed as the AQZ-10 solid-state relays consist of an LED and photo-senstive MOSFET circuit. With no light from the photo MOSFET the FET does not conduct. Without power to the board, the LED will not illuminate. So the "unpowered" fail-safe condition is assured.

·	On power-up the system remains in a fail-safe condition (high impedance/non-conducting) state until explicitly programmed to enter a low-impedance/conducting state.

·	When explicitly told to reset, the system enters a fail-safe condition.

·	When an anamolous condition (watchdog timeout) occurs, the system enters a fail-safe condition.

To handle the power-on reset requirement, the board includes a DS1834 power-on reset IC (with push-button input). The DS1834 provide three ways of generating a power-on reset signal:

1.	A power-on condition on a 5V power supply,

2.	A power-on condition on a 3.3V power supply, or

3.	An explicit reset request on a push-button input.

In the default state the PPSSR-16 uses the first and third modes on to DS1834 to put the system in a "fail-safe" state.

Important note: there are several variants of the DS1834 IC. The DS1834 (no suffix) has an active-low RST output. The DS1834A has an open-collector RST output. The DS1834D has an active-high RST output.  The PPSSR-16 design utilizes the DS1834 (active-low) version.

The PPSSR-16 uses a 5V power supply. Therefore, by default, the PPSSR-16 uses the 5V side of the DS1834 to produce a power-on reset. The PPSSR-16 board programs the DS1834 with a 10% tolerance. So if the voltage drops below (approximately) 4.5 volts (assuming a true 5V input) the chip with generate a reset pulse when power resumes.  As it turns out, both the 5V and 3.3V sides of the chip will accept up to 5.5V on their input pins. The only difference is when they will produce a reset condition (4.5V or 3.0V). If your 5V power supply input to the PPSSR-16 is right on the edge of 4.5V and you're getting spurious resets from the DS1834, you can choose to use the 3.3V power-on-reset function rather than the 5V power-on-reset function. This is accomplished using the DS1834SEL jumpers on the PPSSR-16 board. Putting jumpers between pins 1 & 3 and pins 2 & 4 programs the device to use the 5V power-on-reset (this is the default). Moving the jumpers to pins 3 & 5 and 4 & 6 programs the DS1834 to use the 3.3V power-on-reset.  Note that you're still feeding 5V to the chip (which, electrically, is okay). By using the 3.3V inputs you're providing a 40% tolerance factor rather than the normal 10% tolerance factor.  In practice, there is almost no reason to do this; you will not normally see voltage drops greater than 10% on the board (and if you have a flakey power supply that doesn't provide a good five volts, you should probably replace that first). However, the option is there if you want it.

The reset output (5VRST or 3.3VRST, depending on the jumpers on DS1834SEL) is fed into a positive edge detector circuit (similar to the BS0 edge detector circuit) and this is connected to the RCK signal line (along with the collector on the BS0 edge detector). If either signal, BS0 or the DS1834 RST output, goes low, you get a negative-going pulse on the RCK (register transfer clock) input to the TPIC6B595 shift register.

Note that the time constant for the DS1834 RST edge detector is much longer than that of the BS0 edge detector (10 mSec for the DS1834 versus 5 µSec for BS0). The DS1834 PBRST input requires an active low-signal for at least 2 mSec. The time constant for the RCK pulse is 10 mSec because it is greater than or equal to the pulse being sent to the DS1834 (that triggers the RST pulse).

If, by some coincidence, both BS0 and the DS1834 RST signals occur are the same time, whomever holds the RCK line down the longest (usually the DS1834) will be the winner. Of course, if the DS1834 RST signal is active, the circuitry is clearing the shift register anyway, so ithe data shifting into the shift register will be irrelevant. One important feature, and in fact the main reason for implementing the edge detectors in the RCK signal circuit, is that the static state of either input signal (DS1834 RST or BS0) does not affect the operation of the other signal. That is, if BS0 is held low (or held high) it doesn't prevent the DS1834 from clocking the TPIC6B595 RCK line. Likewise, if the PBRST is held low (or high) it doesn't prevent BS) from generating a clock on the RCK line. Had this been just the logical NAND of the two signals, errant software could leave the BS0 line low (for example) and then the DS1834 circuit would not be able to clear the shift register and shift those zeros into the output latch (putting the system in fail-safe mode).

Note that there is no feedback to the DAQ system (other than putting the output latches on the PPSSR-16 into fail-safe mode) that there has been a power failure and reset on the PPSSR-16 board. If this is a possibility in your system design, you will need to add monitoring circuitry to check for this.

The PPSSR-16 synthesizes the DS1834 input PBRST signal from two PPDO input signals: WD_LATCH and RESET. The WD_LATCH signal is active low whenever the watchdog timer has expired, the RESET signal (not to be confused with the DS1834 RST output) is active low whenever the DAQ_IF CPU module programs the system to do a reset operation.

The PPSSR-16 circuit feeds the WD_LATCH and RESET signals into edge detector circuits and combines their outputs to feed the PBRST input on the DS1834 IC.

Note that this circuit inverts the two input signals. Therefore, the positive-edge detector circuits are actually producing pulses on the negative-going edges of these two signals (that is, on the leading edge of the RESET and WD_LATCH pulses, which are normally active-low pulses). Because the PBRST input on the DS1834 IC requires an active-low signal at least 2 mSec in duration, the time constants on the two edge detector circuits is 10 mSec. This means that these signals should be held low for at least 10 mSec to guarantee a full 10 mSec output pulse.

Note that pulsing (low) the RESET or WD_LATCH line will (eventually) generate a pulse on the RCK line. This, alone, however, does not put the system into the fail-safe state. Pulsing RCK will transfer the current data from the TPIC6B595 shift register to the output latch; however, if the contents of the shift register are not zero this will not produce a fail-safe output condition. Therefore, activation of either RESET or WD_LATCH must also clear the shift register prior to transfering the data from the shift register to the output latch. The system must pulse (low) the TPIC6B595 SRCLR line to clear the contents of the shift register. Sadly, the SRCLR input only clears the shift register. It does not (asynchronously) also clear the output latch. This is a shame, almost all the edge detection circuitry used to synthesize RCK could have gone away if SRCLR cleared the output latch as well as the shift register.

The PBRST signal is almost the signal needed to accomplish this. PBRST goes low whenever RESET or WD_LATCH become active. Furthermore, this signal will be low prior to the RCK clock pulse that PBRST generates, so the timing is perfect for the TPIC6B595 chip:

The only problem here is that to clear the TPIC6B595 shift register requires a rising edge on the PBRST line. Because of the edge detector circuitry, this rising edge is pretty much guaranteed around 10 mSec after PBRST first goes low because it is totally dependent upon the RC time constant in the two edge detectors (C5*R40 or C3*R37 in the previous schematic). For the reset signal, this is no big deal because software generates the reset pulse (and failure of the software to bring the reset signal high won't affect the behavior of this circuit).

The WD_LATCH signal, however, is generated in hardware (a watchdog timeout on the DAQ_IF board). This signal is set low whenever the watchdog timer times out and remains low until the CPU module on the DAQ_IF explicitly resets it to high by toggling the RESET line. Note that refreshing the watchdog timer (by pulsing the WD_RFSH line on the DAQ_IF board) will not clear the WD_LATCH low condition. Only an explicit active low signal on the RESET signal will set the WD_LATCH signal back to high. For most situations, a system designer would probably like to keep the output latches in their fail-safe state as long as the WD_LATCH signal persists. Some additional circuitry exists in the PPSSR-16 design to allow this:

This circuit includes a 3-pin header that allows the system designer to select PBRST-only operation (only clearing the shift register on while PBRST is active low) or a combination PBRST or WD_LATCH active-low condition. If there is a jumper between pins 1 & 2 on the SCLR header, the system only resets the shift register while PBRST is low. If there is a jumper between pins 2 & 3 on the SCLR header, then the system will keep SRCLR held low as long as PBRST is low or WD_LATCH is low. By default, the boards have pins 2 & 3 jumpered, so as long as WD_LATCH is low the circuit will hold SRCLR low as well.

Remember that holding SRCLR low will only clear the shift register, not the output latch, on the TPIC6B595 IC. When WD_LATCH goes low this will clear the shift register (and keep it clear as long as WD_LATCH is low) and, ultimately, send a pulse to the RCK line to shift the data to the output latch. Continuing to hold the SRCLR line low will not generate any additional RCK pulses. However, should the software attempt to shift in additional data (by placing the data on MOSI, toggling SPI-CLK, and pulsing BS0 appropriately) holding the SRCLR line low will keep the input shift register in a cleared state so that when the rising edge of BS0 arrives the shift register is still clear and the output latch will remain in a fail-safe state.

It is hard to imagine a situation (in a fail-safe system) where you would want to disable the WD_LATCH low feature, but if this is what you need you can always put the jumper on pins 1 & 2 of the SCLR header.

4.4.5	PPSSR-16 Outputs and Output LEDs

24:	[DAQ_HDD_024]

The PPSSR-16 implements the 16 output channels using two 8-bit TPIC6B595 shift registers. The output pins on the TPIC6B595 (Drain0..Drain7) are open-drain FETs capable of sinking up to 150 mA each. Each of these lines (call it Dtrl) is fed to a solid-state relay and LED/resistor circuit:

Programming an output bit (Drainn) with a '1' produces a low-impedance condition to ground. This will cause current to flow from Vcc through the LED (illuminating the LED) as well as current to flow through the SSR (and through the LED inside it) to ground. This, coincidentally, creates a low-impedance (closed) circuit across the DOUT terminals. Programming an output bit with a '0' creates a high-impedance state in the TPIC6B595 channel's FET, thus prevent current from flowing through these two LEDs. This produces a high-impedance state across the DOUT terminals (effectively creating an open circuit).

The circuit above is replicated 16 times for each of the 16 channels on the PPSSR-16:

Please be aware that the RB0..RB15 signals from the two TPIC6B595 chips do not directly correspond to digital outputs D0..D16 on the PPSSR-16 board. The output pins were routed to the closest solid-state relays on the board to improve the quality of the circuit board layout. It is up to the software to translate bit positions shifted in to the corresponding outputs on the PPSSR-16 circuit board. This, of course, is always subject to change with revisions of the circuit board.

The PPSSR-16 design uses AQZ-10 Form A Solid-State Relay modules. This SSRs provide up to 2A current at 30 VDC. Each SSR is connected to a two-pin screw terminal for interface to external devices.

In order to achieve a full 2A control, the traces on the circuit board should be at least 50 mil wide and there should be traces on the top and bottom sides of the boards to allow for as much heat dissipation as possible (this size keeps the PCB temperature rise well below 10C). Note that standard engineering practice dictates derating the current to ½ the maximum rating (i.e., 1A), so 50 mil traces (particularly, two of them) will more than handle this. Note that Rev 3 of the PPSSR-16 circuit board actually uses 100 mil traces on the top and bottom layers.  This design doesn't put copies of the traces on the interior layers because of heat dissipation issues. With 1oz copper, traces top and bottom are more than sufficient.

As per the TPCI6B595 data sheet, pins 1, 10, 11, 19, and 20 should be soldered to a large pad to serve as a heatsink for the device. In addition, to improve heat flow to this heatsink, the TPIC6B595 IC should be solder directly to the board (do not use a socket). The underlying copper connected to these pins should not use "thermals" (cross-hatches rather than solid copper connections) as the whole point is to move heat away from these pins as efficiently as possible. Of course, this will make soldering (and desoldering, if it comes to that) a bit more difficult; however, having the solid thermal connection will improve the life of the chip.

4.4.6	PPSSR-16 Buffered Signal Lines

25:	[DAQ_HDD_025]

The PPSSR-16 may not present more than one TTL load to any bus signal passed along the PPDO bus to multiple boards. for this reason, the PPSSR-16 board includes a quad tri-state buffer chip (74HC125) that buffers the following four signals:

·	BS0

·	SPI-CLK (SCK)

·	RESET (RST)

·	WD_LATCH

Technically, the SPI-CLK (SCK) signal should be gated by the BS0 line to avoid shifting in garbage while the DAQ system is communication on other SPI busses (e.g., the PPDIO96 bus). However, it doesn't harm anything to shift garbage through the shift registers if the system never transfers the data to the output latch (via the BS0 signal). The PPSSR-16 board only shifts data on the rising edge of the BS0 signal (which occurs, presumably, after the software has shifted valid data into the shift registers) or when a RESET or WD_LATCH signal occurs (in which case SRCLR has been pulled low and any garbage shifted in has been cleared).

4.5	PPRELAY-12 12-Channel Mechanical Relay Board

4.5.1	Capacity and Interface

26:	[DAQ_HDD_026]

The PPRELAY-12 board provides 12 channels of mechanical relay control for digital output devices. It also provides 4 bits of open-drain high current (sinking: 150 mA per pin) digital I/O. It provides 12 sets of screw terminals (three terminals each: NO/COM/NC – normally open/common/normally close) as outputs and a pair of 10-pin (2x5) headers that connect to the PPDO connector on the DAQ_IF board and provide a daisy-chain output to another output board.

The board utilizes JZC-11F-05VDC – 1Z relays that contain both normally open and normally closed contacts. There are board-layout-compatible relays available that drop the NC contact (providing only a normally-open contact) as well.

The PPDO input connector is a 10-pin header (2x5) with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Output: BS0 (SPI Chip Select) | 2 | N/C |
| 3 | Input: MISO (SPI input) | 4 | Output: MOSI (SPI output) |
| 5 | Output: SPI Clk | 6 | I/O: J2_38 |
| 7 | Output: RESET | 8 | Output: WD_LATCH |
| 9 | Input: IRQ | 10 | Gnd |

The PPDO output connector is nearly identical, with the following signals:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Output: BS0 (SPI Chip Select) | 2 | Vcc |
| 3 | Input: MISO (SPI input) | 4 | Output: MOSI (SPI output) |
| 5 | Output: SPI Clk | 6 | I/O: J2_38 |
| 7 | Output: RESET | 8 | Output: WD_LATCH |
| 9 | Input: IRQ | 10 | Gnd |

The differences are on Pin 2 and pin 4. The input connector (+5V from the previous board in the daisy-chain) is left disconnected on the input connector. Pin 2 is connected to Vcc (+5V) on the output connector. Pin 4 on the input connector is tied to the serial in pin of the first TPIC6B595 serial shift register. Pin 4 on the output connector is tied to the serial out pin of the second TPIC6B595 IC (Serial data flows into the first shift register, out of the first and into the second shift register, and then out of the second shift register and to the output connector).

As the PPRELAY-12 board is a digital-output-only board, the PPRELAY-12 ignores the MISO input pin.

4.5.2	Power Supply

27:	[DAQ_HDD_027]

The PPRELAY-12 receives +5V power and ground on a two-pin screw terminal. As with most DAQ system boards, there is an LED connected to the power supply to indicate when power is applied.

The greatest power use on the board will be the current required to actuate the mechanical relays. The JZC-11F-05VDC – 1Z relay has a nominal coil resistance of 320 Ω. At 5V the coils will draw less than 20 mA. Therefore, absolute worst case, is 12* 20mA or 240 mA of current actuate all relays.   In addition to the relay coil, there is an LED associated with each output channel that illuminates whenever the SSR is actuated. These LEDs have a 470 Ω resistor, so each LED will also consume just under 15 mA. Of course, the rest of the board also draws current, so it's not unreasonable to expect upwards of 500-600 mA to be pulled from the power supply when all relays are actuated.

Note that the power switched by the relays is (theoretically) independent of the power supplied to the board. Unless you are powering some external circuit being switched by the relays from the PPRELAY-12's power supply, their power usage doesn't count towards the power used by the board.

4.5.3	PPRELAY-12 Board Select Signal (BS0) and Clocking Data into the PPRELAY-12

28:	[DAQ_HDD_028]

The PPRELAY-12 contains three input signal lines that control shifting data into the TPIC6B595 shift register and transferring that data to the output latches: BS0, SPI-CLK, and MOSI. These three signals correspond to three of the four SPI control lines (CS, SCK, and MOSI; as an output line the fourth SPI control line, MISO, is not used).

Note: although the PPRELAY-12 board uses the SPI control lines, the PPRELAY-12 isn't, technically speaking, an SPI device. It just so happens that the SPI clock and MOSI lines work fine as inputs to the TPIC6B's shift in and clock inputs. This "grand coincidence" allows the DAQ system to use the SPI bus to control shift-register-based digital output boards (e.g., PPSSR-16 and PPRELAY-12) on the system SPI bus.

To shift data into the two TPIC6B595 shift registers on the PPRELAY-12, the system should first switch the BS0 (board select 0) from high to low. The BS0 signal must be held low for the entire shift duration. Note that if you connect multiple PPRELAY-12 (and PPRELAY-12) boards in a daisy-chain on a single PPDO bus (i.e., off a single DAQ_IF board) then you must hold BS0 low while shifting out the bits for all boards. For example, if you have three output boards connected in a daisy chain, you need to hold BS0 low while shifting out all 48 bits for the three boards. Although PPRELAY-12 board possess only 12 relays, they are still 16-bit boards. Four of the output bits are sent to a header rather than controlling relays. Therefore, you must shift 16 bits for each board, regardless of whether it is a PPSSR-16 or PPRELAY-12 board.

The TPIC6B595 shift registers shift the data present on the SER_IN pin into the shift register on the rising edge of the SRCK (SPI-CLK) signal. As in turns out, this is the exact waveform you want when transmitting data on the SPI bus. The bit shifted out appears on the SER_OUT pin that you normally feed to the input of any additional TPIC6B595 ICs in the chain.

On the rising edge of the BS0 signal, the PPRELAY-12 boards copy the bits in the shift register over to the output latch. To transfer the bits, a rising-edge clock signal must appear on the TPIC6B595 RCK input. The PPRELAY-12 synthesizes this clock by putting a positive-edge detection circuit on the BS0 input:

On the rising edge of the BS0 signal the transistor momentarily (about 5 µSec = C6 * R35) conducts pulling the RCK signal low for that time period. On the rising edge of that 5 µSec pulse (which occurs at least 5 µSec after BS0 has gone high) the TPIC6B595 shift register copies the data from the input shift register to the output latch.

4.5.4	PPRELAY-12 Power-On Reset, Watchdog Latch, and the Reset Signal

29:	[DAQ_HDD_029]

The PPRELAY-12 board, by requirement, must enter a "fail-safe mode" whenever power is first applied, whenever there is an explicit reset operation (a low pulse on the reset pin), or whenever the DAQ system has a watchdog timeout (low signal on the WD_LATCH input pin).

A "fail-safe mode" is defined as follows:

·	If no power is applied to the PPRELAY-12 board, the  JZC-11F-05VDC – 1Z relays remain in a deengergized (normally open) state. This state is guaranteed as the coils with no power level the relays normally open so the "unpowered" fail-safe condition is assured.

·	On power-up the system remains in a fail-safe condition (deengergized relays) state until explicitly programmed to enter an engergized (closed) state.

·	When explicitly told to reset, the system enters a fail-safe condition.

·	When an anamolous condition (watchdog timeout) occurs, the system enters a fail-safe condition.

To handle the power-on reset requirement, the board includes a DS1834 power-on reset IC (with push-button input). The DS1834 provide three ways of generating a power-on reset signal:

4.	A power-on condition on a 5V power supply,

5.	A power-on condition on a 3.3V power supply, or

6.	An explicit reset request on a push-button input.

In the default state the PPRELAY-12 uses the first and third modes on to DS1834 to put the system in a "fail-safe" state.

Important note: there are several variants of the DS1834 IC. The DS1834 (no suffix) has an active-low RST output. The DS1834A has an open-collector RST output. The DS1834D has an active-high RST output.  The PPRELAY-12 design utilizes the DS1834 (active-low) version.

The PPRELAY-12 uses a 5V power supply. Therefore, by default, the PPRELAY-12 uses the 5V side of the DS1834 to produce a power-on reset. The PPRELAY-12 board programs the DS1834 with a 10% tolerance. So if the voltage drops below (approximately) 4.5 volts (assuming a true 5V input) the chip with generate a reset pulse when power resumes.  As it turns out, both the 5V and 3.3V sides of the chip will accept up to 5.5V on their input pins. The only difference is when they will produce a reset condition (4.5V or 3.0V). If your 5V power supply input to the PPRELAY-12 is right on the edge of 4.5V and you're getting spurious resets from the DS1834, you can choose to use the 3.3V power-on-reset function rather than the 5V power-on-reset function. This is accomplished using the DS1834SEL jumpers on the PPRELAY-12 board. Putting jumpers between pins 1 & 3 and pins 2 & 4 programs the device to use the 5V power-on-reset (this is the default). Moving the jumpers to pins 3 & 5 and 4 & 6 programs the DS1834 to use the 3.3V power-on-reset.  Note that you're still feeding 5V to the chip (which, electrically, is okay). By using the 3.3V inputs you're providing a 40% tolerance factor rather than the normal 10% tolerance factor.  Unlike the PPSSR-16 board (described earlier in this document) there may be good reason to use the 3.3V side of the DS1834. As you engergize each relay coil, you'll see a small voltage drop on the Vcc plane. With 12 relays, it's actually possible to drop the voltage to below 4.5V and cause the DS1834 to go into continuous reset mode.

Note: Severe voltage drops as just described can be avoided by doing two things: first, ensure that heavy gauge wiring (20 ga or better) connects the PPRELAY-12 board to a good +5V power source; second, use of 2 oz copper for the PCB can also help reduce voltage drops on the power plane (though, technically, the 2 oz is really desireable for the relay contact traces).

The reset output (5VRST or 3.3VRST, depending on the jumpers on DS1834SEL) is fed into a positive edge detector circuit (similar to the BS0 edge detector circuit) and this is connected to the RCK signal line (along with the collector on the BS0 edge detector). If either signal, BS0 or the DS1834 RST output, goes low, you get a negative-going pulse on the RCK (register transfer clock) input to the TPIC6B595 shift register.

Note that the time constant for the DS1834 RST edge detector is much longer than that of the BS0 edge detector (10 mSec for the DS1834 versus 5 µSec for BS0). The DS1834 PBRST input requires an active low-signal for at least 2 mSec. The time constant for the RCK pulse is 10 mSec because it is greater than or equal to the pulse being sent to the DS1834 (that triggers the RST pulse).

If, by some coincidence, both BS0 and the DS1834 RST signals occur are the same time, whomever holds the RCK line down the longest (usually the DS1834) will be the winner. Of course, if the DS1834 RST signal is active, the circuitry is clearing the shift register anyway, so ithe data shifting into the shift register will be irrelevant. One important feature, and in fact the main reason for implementing the edge detectors in the RCK signal circuit, is that the static state of either input signal (DS1834 RST or BS0) does not affect the operation of the other signal. That is, if BS0 is held low (or held high) it doesn't prevent the DS1834 from clocking the TPIC6B595 RCK line. Likewise, if the PBRST is held low (or high) it doesn't prevent BS) from generating a clock on the RCK line. Had this been just the logical NAND of the two signals, errant software could leave the BS0 line low (for example) and then the DS1834 circuit would not be able to clear the shift register and shift those zeros into the output latch (putting the system in fail-safe mode).

Note that there is no feedback to the DAQ system (other than putting the output latches on the PPRELAY-12 into fail-safe mode) that there has been a power failure and reset on the PPRELAY-12 board. If this is a possibility in your system design, you will need to add monitoring circuitry to check for this.

The PPRELAY-12 synthesizes the DS1834 input PBRST signal from two PPDO input signals: WD_LATCH and RESET. The WD_LATCH signal is active low whenever the watchdog timer has expired, the RESET signal (not to be confused with the DS1834 RST output) is active low whenever the DAQ_IF CPU module programs the system to do a reset operation.

The PPRELAY-12 circuit feeds the WD_LATCH and RESET signals into edge detector circuits and combines their outputs to feed the PBRST input on the DS1834 IC.

Note that this circuit inverts the two input signals. Therefore, the positive-edge detector circuits are actually producing pulses on the negative-going edges of these two signals (that is, on the leading edge of the RESET and WD_LATCH pulses, which are normally active-low pulses). Because the PBRST input on the DS1834 IC requires an active-low signal at least 2 mSec in duration, the time constants on the two edge detector circuits is 10 mSec. This means that these signals should be held low for at least 10 mSec to guarantee a full 10 mSec output pulse.

Note that pulsing (low) the RESET or WD_LATCH line will (eventually) generate a pulse on the RCK line. This, alone, however, does not put the system into the fail-safe state. Pulsing RCK will transfer the current data from the TPIC6B595 shift register to the output latch; however, if the contents of the shift register are not zero this will not produce a fail-safe output condition. Therefore, activation of either RESET or WD_LATCH must also clear the shift register prior to transfering the data from the shift register to the output latch. The system must pulse (low) the TPIC6B595 SRCLR line to clear the contents of the shift register. Sadly, the SRCLR input only clears the shift register. It does not (asynchronously) also clear the output latch. This is a shame, almost all the edge detection circuitry used to synthesize RCK could have gone away if SRCLR cleared the output latch as well as the shift register.

The PBRST signal is almost the signal needed to accomplish this. PBRST goes low whenever RESET or WD_LATCH become active. Furthermore, this signal will be low prior to the RCK clock pulse that PBRST generates, so the timing is perfect for the TPIC6B595 chip:

The only problem here is that to clear the TPIC6B595 shift register requires a rising edge on the PBRST line. Because of the edge detector circuitry, this rising edge is pretty much guaranteed around 10 mSec after PBRST first goes low because it is totally dependent upon the RC time constant in the two edge detectors (C5*R40 or C3*R37 in the previous schematic). For the reset signal, this is no big deal because software generates the reset pulse (and failure of the software to bring the reset signal high won't affect the behavior of this circuit).

The WD_LATCH signal, however, is generated in hardware (a watchdog timeout on the DAQ_IF board). This signal is set low whenever the watchdog timer times out and remains low until the CPU module on the DAQ_IF explicitly resets it to high by toggling the RESET line. Note that refreshing the watchdog timer (by pulsing the WD_RFSH line on the DAQ_IF board) will not clear the WD_LATCH low condition. Only an explicit active low signal on the RESET signal will set the WD_LATCH signal back to high. For most situations, a system designer would probably like to keep the output latches in their fail-safe state as long as the WD_LATCH signal persists. Some additional circuitry exists in the PPRELAY-12 design to allow this:

This circuit includes a 3-pin header that allows the system designer to select PBRST-only operation (only clearing the shift register on while PBRST is active low) or a combination PBRST or WD_LATCH active-low condition. If there is a jumper between pins 1 & 2 on the SCLR header, the system only resets the shift register while PBRST is low. If there is a jumper between pins 2 & 3 on the SCLR header, then the system will keep SRCLR held low as long as PBRST is low or WD_LATCH is low. By default, the boards have pins 2 & 3 jumpered, so as long as WD_LATCH is low the circuit will hold SRCLR low as well.

Remember that holding SRCLR low will only clear the shift register, not the output latch, on the TPIC6B595 IC. When WD_LATCH goes low this will clear the shift register (and keep it clear as long as WD_LATCH is low) and, ultimately, send a pulse to the RCK line to shift the data to the output latch. Continuing to hold the SRCLR line low will not generate any additional RCK pulses. However, should the software attempt to shift in additional data (by placing the data on MOSI, toggling SPI-CLK, and pulsing BS0 appropriately) holding the SRCLR line low will keep the input shift register in a cleared state so that when the rising edge of BS0 arrives the shift register is still clear and the output latch will remain in a fail-safe state.

It is hard to imagine a situation (in a fail-safe system) where you would want to disable the WD_LATCH low feature, but if this is what you need you can always put the jumper on pins 1 & 2 of the SCLR header.

4.5.5	PPRELAY-12 Outputs and Output LEDs

30:	[DAQ_HDD_030]

The PPRELAY-12 implements the 16 output channels using two 8-bit TPIC6B595 shift registers. The output pins on the TPIC6B595 (Drain0..Drain7) are open-drain FETs capable of sinking up to 150 mA each. Each of these lines (call it Dtrl) is fed to a solid-state relay and LED/resistor circuit:

Programming an output bit (Drainn) with a '1' produces a low-impedance condition to ground. This will cause current to flow from Vcc through the LED (illuminating the LED) as well as current to flow through the relay coil to ground.  Programming an output bit with a '0' creates a high-impedance state in the TPIC6B595 channel's FET, thus prevent current from flowing through the LED and relay coil.

Note that the circuit includes a flyback diode across the relay coil. In theory, the TPIC6B595 includes this diode as part of the package. The documentation for the TPIC6B595 makes the following statement:

The device contains a built-in voltage clamp on the  outputs for inductive transient protection. Power  driver applications include relays, solenoids, and other medium current or high-voltage loads.

Of course, no design engineer in their right mind wouldn't automatically place a flyback diode in the circuit despite the data sheet claim. Hence their presence in this circuit.

The circuit above is replicated 12 times for each of the 12 channels on the PPRELAY-12:

The remaining four bits from the second TPIC6B595 IC are sent to an auxiliary output header providing extra digital output capabilities. Each pin on this connector is capable of sinking 150 mA of current.

Please be aware that the RB0..RB15 signals from the two TPIC6B595 chips do not directly correspond to digital outputs D0..D15 on the PPRELAY-12 board. The output pins were routed to the closest relays on the board to improve the quality of the circuit board layout. It is up to the software to translate bit positions shifted in to the corresponding outputs on the PPRELAY-12 circuit board. This, of course, is always subject to change with revisions of the circuit board.

As per the TPCI6B595 data sheet, pins 1, 10, 11, 19, and 20 should be soldered to a large pad to serve as a heatsink for the device. In addition, to improve heat flow to this heatsink, the TPIC6B595 IC should be solder directly to the board (do not use a socket). The underlying copper connected to these pins should not use "thermals" (cross-hatches rather than solid copper connections) as the whole point is to move heat away from these pins as efficiently as possible. Of course, this will make soldering (and desoldering, if it comes to that) a bit more difficult; however, having the solid thermal connection will improve the life of the chip.

The PPRELAY-12 design uses JZC-11F-05VDC – 1Z Relay modules. These relays provide up to 5A current at 30 VDC with a very high isolation from the reset of the circuit.  In order to achieve a full 5A control, the traces on the circuit board should be at least 100 mil wide and there should be traces on the top and bottom sides of the boards to allow for as much heat dissipation as possible (this size keeps the PCB temperature rise well below 10C). You will also want to use 2 oz copper boards in the design for additional current-carrying capability. Note that standard engineering practice dictates derating the current to ½ the maximum rating (i.e., 2.5A), so 100 mil traces (particularly, two of them) will more than handle this.  This design doesn't put copies of the traces on the interior layers because of heat dissipation issues. With 2 oz copper, traces top and bottom are more than sufficient.

4.5.6	PPRELAY-12 Buffered Signal Lines

31:	[DAQ_HDD_031]

The PPRELAY-12 may not present more than one TTL load to any bus signal passed along the PPDO bus to multiple boards. for this reason, the PPRELAY-12 board includes a quad tri-state buffer chip (74HC125) that buffers the following four signals:

·	BS0

·	SPI-CLK (SCK)

·	RESET (RST)

·	WD_LATCH

Technically, the SPI-CLK (SCK) signal should be gated by the BS0 line to avoid shifting in garbage while the DAQ system is communication on other SPI busses (e.g., the PPDIO96 bus). However, it doesn't harm anything to shift garbage through the shift registers if the system never transfers the data to the output latch (via the BS0 signal). The PPRELAY-12 board only shifts data on the rising edge of the BS0 signal (which occurs, presumably, after the software has shifted valid data into the shift registers) or when a RESET or WD_LATCH signal occurs (in which case SRCLR has been pulled low and any garbage shifted in has been cleared).

4.6	PPAIO-16/4 16-Channel Analog Input/4-Channel Analog Output Board

4.6.1	Capacity, Interface, and Accuracy

32:	[DAQ_HDD_032]

The PPAIO-16/4 board provides uses four ADS1115 modules to provide 16 channels of unsigned 15-bit single-ended analog input (four input channels per ADS1115).  Alternately, a system designer may combine pairs of analog inputs to obtain up to 8 channels of signed 16-bit double-ended analog input. The ADS1115 ADCs provide a programmable gain amplifier supporting input voltages of 0..5V, 0..4.096V, 0..2.048V, 0..1.024V, 0..0.512V, or 0..0.256V. Normally, the DAQ system operates these chips in the 0..4.096V range as this is the voltage range produced by the PPAC-4 analog conditioning modules. Note that the full 16-bit input range is only available when using double-ended inputs; the single-ended inputs do not allow negative numbers and are limited to 15 bits.

The ADS is capable of processing as many as 860 samples/second. It may, however, be operated at a lower sample rate with higher accuracy. The requirements only call for 100 SPS, so operating at the ADS1115 default rate of 128 SPS is perfectly reasonable.

The PPAIO-16/4 also supports up to four MCP4725  DAC modules with additional analog amplification (on board) to convert the DAC's 12-bit 0..5V analog output to the range -10..+10V. The DAC's output sample rate is largely determined by the I2C interface, which (while slow) is certainly capable of exceeding the 100 SPS output rate specified by the requirements.

The accuracy of the ADS1115 IC greatly exceeds that of the circuit board layout. The system requirements call for 5% accuracy. In practice such a low accuracy was specified to allow automated testing using the DAC output to feed the ADC inputs. Given that such a test fixture is going from a 12-bit (unsigned) output voltage to a 15-bit (unsigned) input voltage with varying reference voltages across the power plane on the circuit board, the 5% was very liberal allowing wide variations between the two chips.

For demo/prototyping purposes, using sockets and headers for the ICs and breakout boards (BoBs) is probably acceptable, but for actual installation everything should be soldered onto PPAIO-16/4 circuit board (the BoBs should have right-angle headers soldered onto them and those headers should be soldered onto the PPAIO-16/4 PCB).

For the quietest and most accurate readings, you should use double-ended inputs and run twisted-pair cables from the signal source (or a PPAC-4 analog conditioning board) to the screw terminal inputs on the PPAIO-16/4 PCB. For convenience, the PPAIO-16/4 board includes a pair of 8-pin (2x4) headers that mate with similar connectors on the PPAC-4 boards. However, if low noise and high accuracy is desireable, do not use these connectors and ribbon cables to connect the PPAC-4 to the PPAIO-16/4 – use twisted pair (and better yet, shielded twisted pair) cabling for the interconnect.

The 8-pin header uses the following pin-out:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | AIN1+ | 2 | GND1 |
| 3 | AIN0+ | 4 | GND0 |
| 5 | AIN3+ | 6 | GND3 |
| 7 | AIN2+ | 7 | GND2 |

(If you're wondering, the out-of-sequence pinout produces cleaner trace paths on the circuit board, avoiding crossing other independent signals.)

One other thing to consider is your power supply. The PPAIO-16/4 runs off a ±12V power supply. This must be a "clean" power supply. Preferably one that is separate from those powering the digital boards in the DAQ system and especially one that is not connected to relay boards or other high-current demand circuits with lots of transients. Such boards will create spikes on the power supply lines that will affect your analog readings.

By following these rules you can obtain much better accuracy than that dictated by the PPAIO-16/4 requirements. Those requirements are suitable for the original intended purpose of the PPAIO-16/4 (various analog inputs from real-world sensors that aren't that accurate). Those requirements are easily improved upon, when needed, by carefully passing analog signals around in your design.

The ADS1115 and MCP4725 ICs and related components are surface mount devices (SMDs). A design goal for the DAQ system is to avoid using SMDs so that the boards can be tested, maintained, modified, and repaired in the field. The exception to this rule is that SMDs in the design are okay if commerically available (open hardware) breakout boards for the chips are available. Adafruit provides breakout boards for both these chips, Sparkfun also provides a BoB for the MCP4725 IC. The DAQ design uses the BoBs from both of these suppliers.

4.6.2	PPAIO-16/4 I2C Interface, Port Assignment, and Daisy-Chaining

33:	[DAQ_HDD_033]

The PPAIO-16/4 board has two I2C bus connections: an input connection and an output connection. The header contains data lines for two independent I2C busses. These connections are 6-pin (2x3) headers with the following pinouts:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | I2C SDA port A (data) | 2 | I2C SDA port B (data) |
| 3 | I2C SCL port A (clock) | 4 | I2C SCL port B (clock) |
| 5 | Gnd | 5 | Gnd |

On a given PPAIO-16/4 the ADC modules only use the A port. The DAC chips use both I2C ports.

The I2C input header pins are not routed directly to the I2C output header pins. Instead, the circuit swaps the Port A and Port B pin between the input and output headers:

This input/output I2C bus arrangement allows you to daisy-chain two PPAIO-16/4 boards on a single DAQ_IF I2C bus connector and the two boards (subject to certain construction limitations) will operate on separate I2C busses.

The ADS1115 ADC chips are I2C bus devices that can operate at one of four separate I2C addresses. A single address pin (ADDR) on the ADS1115 connects to one of the following pins (also on the ADS1115) to select one of the following addresses:

·	ADDR to Gnd: I2C address 0x48 on I2C bus A

·	ADDR to Vcc (+5v): I2C address 0x48 on I2C bus A

·	ADDR to SDA: I2C address 0x4a on I2C bus A

·	ADDR to SCL: I2C address 0x4b on I2C bus A

There are four Adafruit ADS1115 modules on each PPAIO-16/4 board (numbered 1..4, corresponding to addresses 0x48 through 0x4b, respectively). Each Adafruit module supports 4 single-ended or two double-ended analog inputs. The corresponding AINn (n=0..15) input port assignments on a single PPAIO-16/5 board are as follows:

| Module # | I2C address | AIN Ports (single-ended) | AIN Ports (double-ended) Double-ended ports connect their positive terminal to AIN0, AIN2, AIN4, AIN6, AIN8, AIN12, or AIN14. They connect their negative terminals to AIN1, AIN3, AIN5, AIN7, AIN9, AIN11, AIN13, or AIN15 (odd/even pairs). Double-ended signals do not use the Gnd pins on the screw terminals. |
| --- | --- | --- | --- |
| 1 | 0x48 | AIN0..AIN3 | AIN0/AIN1, AIN2/AIN3 |
| 2 | 0x49 | AIN4..AIN7 | AIN4/AIN5, AIN6/AIN6 |
| 3 | 0x4a | AIN8..AIN11 | AIN8/AIN9, AIN10/AIN11 |
| 4 | 0x4b | AIN12..AIN15 | AIN12/AIN13, AIN14/AIN15 |

When you have two PPAIO-16/4 boards daisy-chained together, the first board (directly connected to the DAQ_IF) responds to I2C addresses on the first (A) I2C bus, the second board (connected to the first PPAIO-16/4) responds to I2C addresses on the second (B) bus.

There are four MCP4725 DAC modules on the PPAIO-16/4 board. As these chips can only respond to two different I2C address, the four modules use both I2C busses. The Adafruit MCP4625 BoBs consume I2C addresses 0x62 and 0x63. The corresponding output port assignments are as follows:

| Module # | I2C address | AOUT Ports |
| --- | --- | --- |
| 1 | 0x62: bus A | AOUT0 |
| 2 | 0x63: bus B | AOUT1 |
| 3 | 0x62: bus A | AOUT2 |
| 4 | 0x63: bus B | AOUT3 |

The MCP4725 BoB modules from Sparkfun use different I2C addresses and have the following output port assignments:

| Module # | I2C address | AOUT Ports |
| --- | --- | --- |
| 1 | 0x60: bus A | AOUT0 |
| 2 | 0x61: bus B | AOUT1 |
| 3 | 0x60: bus A | AOUT2 |
| 4 | 0x61: bus B | AOUT3 |

To select between the two addresses (0x60/0x61 or 0x62/0x63) you connect the ADDR pin on the MCP4725 to Vcc (+5V) or Gnd. Connecting ADDR to Vcc selects the odd address of the pair, connecting ADDR to Gnd (or left floating) selects the even address:

| ADDR tied to: | Adafruit address | Sparkfun address |
| --- | --- | --- |
| Gnd | 0x62 | 0x60 |
| Vcc | 0x63 | 0x61 |

Note that the ADDR pin is accessed differently on the Adafruit and Sparkfun MCP4725 modules. On the Adafruit BoB the ADDR pin is brought out to one of the header pins; on the Sparkfun board the ADDR pin is accessible via a pair of solder pads on the circuit board.

If you daisy-chain two PPAIO-16/4 boards on the same DAQ_IF I2C bus, the first board must have Adafruit MCP4725 DAC BoBs installed and the second must have Sparkfun MCP4725 DAC BoBs installed. This prevents I2C address conflicts. Technically, you could install two Adafruit and two Sparkfun BoBs on a single board and have that board operate off a single I2C bus. While this might make better sense from a certain point of view, the current design allows you to install four PPAIO-16/4 boards in the system (no daisy-chaining) utilizing parts bought from a single vendor (Adafruit). Note that other topologies are possible. However, the software written for the DAQ system assumes all Adafruit or all Sparkfun DACs on the same board and Adafruit DACs on the first board and Sparkfun DACs on the second. As a general rule, you should connect the first four PPAIO-16/4 boards directly to the DAQ_IF board and only daisy-chain them if you need more than four PPAIO-16/5 boards in the system (the standard software expects this topology).

Note that the PPAIO-16/4 board doesn't bother buffering the I2C lines. This is largely because there are never more than a few I2C devices on each I2C bus (e.g., 4 ADCs and 4 DACs) so the buffering isn't really necessary.

4.6.3	PPAIO-16/4 Power Supply

34:	[DAQ_HDD_034]

The PPAIO-16/4 receives ±12V power and ground on a three-pin screw terminal. As with most DAQ system boards, there is an LED (indirectly) connected to the +12V power supply to indicate when power is applied.

Because the Adafruit and Sparkfun breakout boards (BoBs) run off +5V, there is a linear voltage regulator on the board (L7805CV) that will convert the +12V supply to +5V. This regulator is good for 1A which is more than sufficient to power the LED, Bobs, and other 5V circuitry.

Because the PPAIO-16/4 involves sensitive analog circuitry (ADCs and DACs are very sensitive to voltage levels and fluctuations) it is very important to supply the board with good, clean, highly-filtered power. There should be no heavy loads (particularly heavy intermittent loads) and certainly no inductive loads (e.g., motors, magnets, or relays) on the same power supply. Even putting digital circuits on the same power supply is not a very good idea. The best solution is to have a dedicated ±12V power supply just for the analog components in the DAQ system.

Because there are four separate power busses on the PPAIO-16/4 board (+5V, +12V, -12V, and Gnd) with only four layers on the circuit board, the non-ground voltages share the same circuit board layer. The power busses were manually laid out to deliver needed voltages wherever necessary without using vias or traces. The only exception to this rule was to use a 100 mil wide trace to deliver +12V to the 5V voltage regulator.

Note that ground planes were placed on the top and bottom layers of the circuit board to provide shielding and help eliminate noise. This is in addition to the ground plane found on the interior of the PCB.

4.6.4	PPAIO-16/4 Analog Output Amplifiers

35:	[DAQ_HDD_035]

The PPAIO-16/4 contains four opamp circuits that convert the 0..5V output from the DAC chips into either a ±5V signal or a ±10V signal (jumper programmable):

The first opamp in this circuit has an adjustable gain (nominally 2) that converts the 0..5V input (from the DAC) to 0..10V (gain is adjustable with the SPAN pot). The second opamp in the circuit (with no jumper installed) allows setting the offset such that the output is ±10V (with no jumper, the gain is 2). Installing the jumper block on the ±5V header halves the feedback resistance (which halves the gain) reducing the output voltage to ±5V.  There are four copies of this circuit on the PPAIO-16/4 – one for each DAC on the board.

Note that the LM324 opamp used in this design easily provides the 1kHz bandwidth and linear response specified by the requirements. The SPAN pot provides a gain (span) adjustment for the circuit and the ZERO pot provides a voltage offset (zero) function.

4.7	PPAC4 4-Channel Analog Conditioning Board

4.7.1	Capacity and Interface

36:	[DAQ_HDD_036]

The PPAC4 board provides four channels of analog conditioning and isolation. Each channel accepts a singled-ended ±10V analog input, isolates it, and converts the input to a double-ended/differential signal (0..4.096V on each side) suitable for input to a PPAIO-16/4 board.

The board provides four two-pin screw terminals as input connectors and also provides four two-pin screw terminals as output connectors.

There is an 8-pin (2x4) header on the board connected to the input signals. This header matches the output header pin-out on the PPAC420 (4-20 mA conversion board) and has the following pin-out:

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | AIN1+ | 2 | GND1 |
| 3 | AIN0+ | 4 | GND0 |
| 5 | AIN3+ | 6 | GND3 |
| 7 | AIN2+ | 7 | GND2 |

(If you're wondering, the out-of-sequence pinout produces cleaner trace paths on the circuit board, avoiding crossing other independent signals.)

There is also an 8-pin (2x4) header containing the four differential output signals. You can use a small ribbon cable to connect the PPAC4 directly to a PPAIO-16/4 board. However, keep in mind that ribbon cables tend to be noisy, so if you are interested in a low-noise connection between the PPAC4 and PPAIO-16/5 boards (or between the PPAC4 and PPAC420 boards), you should use a twisted pair cable between screw terminals on the boards. In theory, using the differential pairs will minimize (if not eliminate) cross talk in the cables, but twisted pairs rather than ribbon cables is always quieter.

PPAC4 8-pin output header pin-out (connection to PPAIO-16/4 board):

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | AIN0+ | 2 | AIN0- |
| 3 | AIN1+ | 4 | AIN1- |
| 5 | AIN2+ | 6 | AIN2- |
| 7 | AIN3+ | 7 | AIN3- |

4.7.2	PPAC4 Power Supply

37:	[DAQ_HDD_037]

The PPAC4  receives ±12V power and ground on a three-pin screw terminal. As with most DAQ system boards, there is an LED connected to the +12V power supply to indicate when power is applied.

Each channel contains an isolation amplifier that requires an isolated ±12V power supply. Therefore, the board contains four isolated power supplies (DC to DC converters) that create ±12V for use by the isolation amplifiers.

Because the PPAC4  involves sensitive analog circuitry (opamp circuits are very sensitive to voltage levels and fluctuations) it is very important to supply the board with good, clean, highly-filtered power. There should be no heavy loads (particularly heavy intermittent loads) and certainly no inductive loads (e.g., motors, magnets, or relays) on the same power supply. Even putting digital circuits on the same power supply is not a very good idea. The best solution is to have a dedicated ±12V power supply just for the analog components in the DAQ system.

Because the PPAC4 electrically isolates the incoming signals from the amplification and power systems, the ground and power planes are somewhat complex on the circuit board. You do not want the circuit board's normal ground and power planes going underneath the isolated signals on the circuit board. This could create inductive and capacitive coupling (granted it's tiny, but present nonetheless) to be avoided in an isolated circuit. Therefore, the power and ground planes on the interior layers underneath each isolated circuit are from the isolated power supply for that particular circuit.

4.7.3	PPAC4 Isolation Amplifier Section

38:	[DAQ_HDD_038]

The PPAC4 contains an ISO122 isolation amplifier for each channel. As noted in the previous section there is an isolated ±12 DC to DC converter, running off the PPAC4's +12V, supplying power to the isolation amplifier.

The PDM1-S12 DC-to-DC converter used in the design requires at least a 10% load to produce a correct voltage output. To achieve this, the PPAC4 design places a pair of 2.2K resistors between the (isolated) ±12V leads and the (isolated) Gnd pin on each PDM1-S12. This consumes about 0.07W and the pair of them consume 0.14W. As the device is a 1W device, this corresponds to about 14% power.

The ISO122 amplifier accepts the isolated analog input and copies it to the isolated output with a gain of 1. The ISO122 is a relatively low-end isolation amplifier. The gain will likely not be exactly one and there might be a voltage offset (positive or negative) added to the signal. The amplifier section following the isolation amplifier will compensate for these issues. The ISO122 offers a 50 kHz bandwidth; this is far more than the 1 kHz bandwidth specified by the PPAC4 requirements.

4.7.4	PPAC4 Amplifier Section

39:	[DAQ_HDD_039]

The PPAC4 contains two amplifier circuits, each consisting of a pair of opamps (all part of an LM324 quad opamp package). The first pair of opamps provides gain (span) and offset (zero) adjustments. They also convert an input signal in the range ±10V to the range ±2.048V. The second pair of opamps accept the ±2.048 output from the first amplifier stage and convert that signal to a pair of differential 0..+4.096V outputs. Note that all opamps operate in a linear fashion, thus satisfying the requirement that the transfer function is linear.

Note that the (nominal) resistor values in the first opamp of the amplifier section have a 50:200 ratio (assuming the span pot is exactly in the middle, producing 50K Ω). This produces a gain of ¼. For a ±10V input, this would produce a ±2.5V output. In fact, the PPAC4 board has to be calibrated to produce a ±2.048V output (which the second state of the amplifier section converts to a 0..4.096V differential signal). The span/gain pot handles the discrepancy. Rather than having the span pot exactly in the middle of the range (and adjusting it to obtain exactly ±2.5V), the idea is to increase the resistance by about 20% additional to bring the output voltage down to ±2.048V.

The second opamp in the circuit exists simply to adjust the offset voltage (that is, to set the zero point). Most likely, the ISO122 isolation amplifier will add some positive or negative offset to the input voltage. Putting the zero pot on a separate opamp helps make it slightly more independent of the gain/span pot. Also, the second opamp reinverts the signal (though this could have also been done in the following double-ended output conversion by simply swapping the signal lines).

The double-ended differential outputs are always positive (with respect to the power supply ground). When representing negative voltages (i.e., -10V to just below 0V) the negative diffierential terminal is greater than the positive differential terminal by the specified voltage. For example, -10V is converted to 4.096V on the negative terminal and 0V on the positive terminal. +10V is converted to 0V on the negative terminal and 4.096V on the positive terminal (note: 4.096V represents a full-scale reading, which corresponds to 10V).

The differential opamp stage (the last two opamps) contains a VREF adjustment pot. This sets the voltage that the system will use to represent 0V on the differential output. The nominal value to shoot for is 2.048V. That is, 2.048V appearing on both sides of the differential output will represent 0V (this generally implies that 4.096V on the negative side with 0V on the positive side represents -10V and 0V on the negative side with 4.096V on the positive side represents +10V, with both sides ranging from 0V to 4.096V (the range of the ADC inputs that provide the maximum precision).

4.8	PPAC420 8-Channel 4-20 mA Analog Input Conditioning Board

4.8.1	Capacity and Interface

40:	[DAQ_HDD_040]

The PPAC420 board provides eight channels of 4-20 mA conversion. Each channel accepts a 4-20 mA input (on two-pin screw terminals) and the board produces eight single-ended voltage outputs in the range -1.25 to 20 mA. Note that a 4 mA input produces a 0V output.

The PPAC40 board produces outputs that would normally be fed as inputs to the PPAC4 board. Because the PPAC420 provides eight channels and the PPAC4 board supports only four channels, it will take two PPAC4 boards to handle all the outputs from the PPAC420. As the outputs from the PPAC4 are differential/double-ended outputs, it will take a single PPAIO-16/4 (which supports 8 double-ended inputs) to handle all the output channels from the PPAC420.

In addition to the two-pin screw terminals, the PPAC420 also provides a pair of 8-pin (2x4) headers containing the analog output signals. These headers are compatible with the 8-pin input headers on the PPAC4 board, allowing a single ribbon cable to connect the two boards (two ribbon cables from the PPAC420 can connect to two PPAC4 boards). Of course, twisted pair wiring from the PPAC420 screw terminal outputs to the PPAC4 screw terminal inputs is probably a tiny bit quieter, but you can use ribbon cables if you don't need an ultra-quiet signal.

4.8.2	PPAC420 Power Supply

41:	[DAQ_HDD_041]

The PPAC420  receives +5V power and ground on a two-pin screw terminal. As with most DAQ system boards, there is an LED connected to the +5V power supply to indicate when power is applied.

Each channel contains an isolation amplifier that requires an isolated ±15V power supply. Therefore, the board contains eight isolated power supplies (DC to DC converters) that create ±15V for use by the RCV420 ICs used on the board. Note that each channel is electrically independent of all the others.

As is the case with nearly all DC-to-DC converters/isolated power supplies, the xxxx converters the PPAC420 uses require a minimum 10% load to produce a well-regulated output. As such there are some load resistors between the ±15V power supplies and ground to provide a minimum load.

Because the PPAC420  involves sensitive analog circuitry it is very important to supply the board with good, clean, highly-filtered power. There should be no heavy loads (particularly heavy intermittent loads) and certainly no inductive loads (e.g., motors, magnets, or relays) on the same power supply. Even putting digital circuits on the same power supply is not a very good idea. The best solution is to have a dedicated +5V power supply just for the analog components in the DAQ system.

4.9	PPRLYIO-12 12-Channel I/O Relay Board

4.9.1	Capacity and Interface

42:	[DAQ_HDD_042]

The PPRLYIO-12 board provides 12 channels of mechanical relay control for digital input/output devices. It provides 12 sets of screw terminals (three terminals each: NO/COM/NC – normally open/common/normally close) as outputs.

The board utilizes JZC-11F-05VDC – 1Z relays that contain both normally open and normally closed contacts. There are board-layout-compatible relays available that drop the NC contact (providing only a normally-open contact) as well.

The PPRLYIO-12 board provides two PPDIO96-bank-compatible 20-pin headers – one containing a set of (TTL-compatible) input signals and one containing a set of output signals (jumper programmable as open collector or TTL-compatible pins). These connectors each have the following pinout:

| PPRLYIO-12 Input and Output Pinouts |
| --- |
| Pin | Description | Pin | Description |
| 1 | D1 | 2 | D0 |
| 3 | D2 | 4 | Gnd |
| 5 | D3 | 6 | Gnd |
| 7 | D4 | 8 | Gnd |
| 9 | D5 | 10 | Gnd |
| 11 | D6 | 12 | Gnd |
| 13 | D7 | 14 | Gnd |
| 15 | D8 | 16 | Gnd |
| 17 | D9 | 18 | Gnd |
| 19 | D10 | 20 | D11 |

The output pins can be (jumper) programmed as open collector or TTL-compatible outputs.  The board uses 1-½  ULN2308 8-channel darlington transistor array packages to control the output pins. An active-high signal on the darlington input creates an open circuit which ties the output pin to ground. By itself, this provide an open-collector circuit. There is a set of 12 pairs of jumpers on a header than provide pullup resistors on each outpt channel. If the jumper is in place, this connects a pullup resistor (10kΩ) to +5V for the corresponding channel. In this case, the output pin produces a TTL-compatible output signal of +5V when the darlingon is not actuated, and Gnd when the darlington is switched on. Note that this effectively inverts the output (producing +5V when the input is low and 0V when the input is high).

The input conectors go to a 3x12 (36-pin) header where jumpers can select the input (directly) or an inverted version of the input. If a jumper is installed across the IIN* and INV* pins, then the jumper selects the output of a 74HC04 hex inverter IC and feeds an inverted version of the signal to the darlington. If a jumper is installed across the IIN* and IN* pins, then an uninverted version of the signal is fed to the darlington input.

Note that if you're operating a given PPRLYIO-12 channel in TTL-compatible mode (that is, the corresponding jumper is installed on the pullups header), then the output signal will normally be inverted. Selecting the IIN* and INV* pins on the polarity header will invert the signal prior to the darlington so that the output produces a signal with the same polarity as the input.

Note: the header is actually 3x12, not 4x12 as the schematic might suggest. The IIN* holes in the circuit board overlap. The schematic was drawn this was to make it easy to show the IIN* signals.

4.9.2	PPRLYIO-12 Power Supply

43:	[DAQ_HDD_043]

The PPRLYIO-12 I/O board runs off a +5V power supply. As with most DAQ system boards, the RLYIO-12 I/O board illuminates an LED when power is applied to the board.

4.9.3	PPRLYIO-12 Relay and Data LED Activation

44:	[DAQ_HDD_044]

The PPRLYIO-12 I/O board includes three ULN2308 8-channel darlington transistor array packages. Half the channels (12) provide buffering to the output connector. The remaining 12 channels control the relays and the channel LEDs on the PPRLYIO-12.

(the collector on the darlington transistor output connects to the RD0 signal in the schematic above.)

When the darlington input is activated (with a logic high signal) the transistor creates a closed circuit that shunts the collector (RD0, above) to ground. This turns on the relay and also turns on the associated data LED. When the darlington input is unactivated (with a logic low signal) the darlington presents an open circuit and no current flows through the LED or relay (meaning the LED is off and the relay is in the inactive position with the NO contact open and the NC contact closed).

As with any inductive circuit, there is a flyback diode across the relay coil terminals to shunt any inductive kickback away from the rest of the circuit (note that the ULN2308 darlington array also includes such diodes, but good design dictates always putting a diode right on the coil terminals, anyway).

By its design, the relay isolates the NC/COM/NO contacts from the rest of the circuit.

The board utilizes JZC-11F-05VDC – 1Z relays that provide up to 5A current handling capability (derated to 2.5A by good engineering design principles plus PCB trace limitations). These relays can also handle up to 30 VDC (actually, they are rated up to 125VAC but DAQ system design limits voltages to 30 VDC).